### Environmental Products Part 1 of 2 
V1.5—14 May 1999
Systems and Options Catalog

Environmental Products Overview

Applications Overview

Product Summary Chart

UPS Systems Overview

Desktop UPS Comparison Chart & Product Positioning

Environmental Products Software

Configuration Tools

UPS & Options Quick Selector

Custom Configuration & System Load Information

On-line UPS Systems

Prestige Desktop Models

Compaq and the names of Compaq products referenced herein are either trademarks and/or service marks or registered trademarks and/or service marks of Compaq.

DIGITAL is a Trademark of Compaq Computer Corporation.

Microsoft, Windows, Windows NT, SQL Server, Office and BackOffice are either trademarks or registered trademarks of Microsoft Corporation.

Intel and Pentium are registered trademarks of Intel Corporation.

Other product and company names mentioned herein may be trademarks and/or service marks of their respective owners.

Compaq’s environmental products solve power-related problems and prevent system downtime and damage from occurring.  For supplementary product information, call 1-800-AT-COMPAQ (1-800-282-6672), and ask for Environmental Products Support or contact a local Environmental Products Representative.

### Environmental Products Summary Chart

O=Full Protection, X=Limited Protection

| Condition | On-line UPS Systems1 | Line Interactive UPS Systems1 | Standby UPS Systems | CDM2 | PDM2 | Surge Supressor TVSS2 |
| --- | --- | --- | --- | --- | --- | --- |
| High energy transients, impulses and spikes | O | X | X2 | - | - | O |
| High/low voltage, sags, surges | O | O1 | X2 | O | - | - |
| Frequency variation | O | X2 | X | - | - | - |
| Electrical noise | O | X | X | X | X | - |
| Power outage | O | O | O | - | - | - |
| Environmental monitoring3 | 3 | X | - | X | X | - |
| Network Monitoring | O | O | - | - | - | - |
| Auto-CPU shutdown | O | O | O | - | - | - |

1	Buck boost circuit, may require battery use

2	Only during power failure when operating on battery and inverter

3	Contact local Environmental Products representative for environmetal monitoring solution

### Power Protection Problems and Solutions—Applications Overview

| Product | Application |
| --- | --- |
| UPS Systems | Power Protection against power loss, other power disturbances, and resultant data damage/loss. |
| Monitoring Software | Protects against system crashes when UPS reaches low battery state, tracks power history and provides notification of power loss or low battery. Some packages will allow real time monitoring and Network Management. Provides operation status of UPS. |
| Network Adapter | Allows management of UPS via SNMP based Network management system. |
| Data Surge TVSS Protection | Protects against data damage/loss from transients entering data communications lines. |
| Power Surge protection | Reduces damaging transients to controllable level at building entrance and clamps voltage to acceptable level at point of use. Should always be used in conjunction with data protection for total protection. When used with UPS, provides extra measure of protection for UPS electronics. |
| Hot Swap Power Pass | Allows safe swap-out of UPS without taking system down. Usually expands receptacle capacity as an added feature. |
| Power Distribution & Conditioning CDM & PDM | Allows flexible means to distribute cabling, monitors and regulates power (regulation on conditioning (CDM) models only); ensures proper wiring and grounding. |

### UPS Systems Overview

Compaq offers a full range of UPS systems to meet a variety of needs ranging from low-cost, dependable protection for the desktop to premium power protection for the most critical applications. See UPS and Options Quick Selector for system load data and recommended UPS.

| System | Technology | Output3Load Range | Output Phases | Available Outlets2 | Input Voltage | Output Voltage |
| --- | --- | --- | --- | --- | --- | --- |
| Desktop Prestige | On-line | 650–2000 VA | 1 | 4 (expandable) | 120 | 120 |
| Prestige 3000 | On-line | 2.5 & 3kVA | 1 | 5 (expandable) | 120, 208, 2401 | 120/208 & 120/2401 |
| Prestige 6000 | On-line | 4.5-6 kVA | 1 | 10 (expandable) | 208,2401 | 120, 120/208 & 120/2401 |
| Powerware Profile | On-line | 8–12 kVA4 | 1 | 4 to 8 | 176–276 | 100/200–120/240 (5 selections) |
| PUPS Plus | On-line | 15–18 kVA | 3 | up to 9 | 176–253 | 100/200–120/240 (5 selections) |
| PUPS Plus | On-line | 24–36 kVA | 3 | via PDU | 176–253 or 480 | 115/200-127/220, 277/4801 |
| MATRIX UPS | Line Interactive | 3–5 kVA | 1 | 6 (expandable) | 208, 2401 | 120/208–120/2401 |
| One-UPS | Standby | 250-600 VA | 1 | 4 | 120 or 2301 | 115 or 2301 |

1.	Model dependent; see specifications

2.	Hardwire output to remote panel also available for office/datacenter models. 15- and 20-Amp outlets on PUPS Plus are duplex type

3.	Prestige and PUPS Plus Models are upgradeable in ranges shown, Desktop Models 650-1000m 1000EXT-1500EXT

4.	Powerware Profile input for 8-12 kVA models is  2 phases

### General Product Positioning

|  | High End Workstations/Low End Servers | Midrange/High End Servers | High End Servers |
| --- | --- | --- | --- |
| On-line Models | Prestige Desktop Models | Prestige Series 3000/6000 | PUPS Plus/Profile Series |

### Desktop UPS Comparison Chart

| Features | Prestige Desktop | One-UPS1 |
| --- | --- | --- |
| Topology | On-line | Standby |
| Power conditioning and voltage regulation | Superior performance | Value performance |
| Equipment selection | High-end workstations, Low end servers, Alpha systems, point of sale, standby generator applications | PC-clients, Internet- working hardware |
| Site conditions | All chronic power aberrations | Occasional brownouts/blackouts |
| VA ranges available | 650–2000 VA | 200–600 VA |
| Upgradable models | Yes; 2 ranges: 650–1000; 1000 EXT—1500 EXT | No |
| Full load battery time (model dependent) | 5–15 minutes; 2–3 hours (Prestige EXT) | 5–10 minutes |
| Rackmount application | Kit available all models | Kit available |
| EIA-2322 | 5 Programmed Settings | No |
| LAN Relay port | Included | Yes, except 200-280 VA |
| Warranty3 | 3 years | 2 years |
| Output V normal operation (120 V units) | 120 V ± 3% | same as utility, 98-102V minimum |
| Transfer to battery (full load) | 85 V and 144 V | <98–103 V sel |
| Audible/visual alarms | Yes | audible only |
| Foreign models (230V) | Yes | Yes |
| Visual load/volt indicator | Yes, LED meter | No |
| Output V on battery | 120 V ± 3% sine wave | 115 V ±5% Step-sine wave |

1.	One UPS models have user replaceable batteries.

2.	EIA-232 serial interface allows remote diagnostics, monitoring, and auto shutdown. LAN relay port allows auto shutdown feature only and does not denote direct network connectivity. Prestige models also include settings for AS400, Novell and 3Comm.

3.	Each UPS system includes “Hot Swap” return-to-factory warranty (batteries included), allowing a new unit to be received within 48 hours and a $25,000 equipment protection guarantee.

### Environmental Products Software Matrix

The following chart shows the available software and the applicable UPS system. Several products are available to support basic UPS monitoring and CPU shutdown. Select the product that meets the requirements of the UPS system and operating platform.  See detailed descriptions below and Software Selection Chart.

| Software Product | Order Number1 | Operating System | Applicable Products | Number of CPU Monitoring Ports | Function |
| --- | --- | --- | --- | --- | --- |
| PowerMon | 4N-JBBBB-xx | See order chart | See order chart | (1) Via Relay contact | Basic monitoring and single system shutdown |
| Multimon 4-port2 | 4N-JMIU4-AA | Packages include PowerMon software for OpenVMS (CD-ROM), TK50), Tru64 UNIX, Windows NT and Novell compatible with network adapters | Prestige and PUPS Plus | Up to 4 ports (relay contact) | Basic monitoring and multi system shutdown |
| Multimon 8-port2 | 4N-JMIU8-AA |  |  | Up to 8 ports (relay contact) |  |
| Multimon 2-port2 | 4N-JMMCR-AA |  |  | Up to 2 ports (relay contacts) includes 3rd smart port for network interface |  |
| Multimon 4-port2 hardware only | 4N-JMIU4-AB | Hardware and cables only |  | Up to 4 ports (relay contacts) |  |
| OnliNet Basic | 4N-AEAES-A | All except OpenVMS; see order chart |  | (1) via EIA 232 | Extended monitoring single system shutdown |
| OnliNet Network | 4N-AEAES-B |  |  |  | Network monitoring multiple system shutdown via network adapter |
| OnliSafe | 4N-AEAES-xx | OpenVMS ; see order chart for other applications | Prestige, PUPS Plus, One-UPS | (1) via relay contacts | Basic monitoring and single system shutdown |

1.	All kits include media documentation, cables, and adaptors

2.	Multimon and Micromon packages include multi-interface unit, 10-foot primary and 25-foot secondary cables and adapters for DB0, DB25 and RJ45 connection.  Multimon packages include splitter cable for smart communications interface. Micromon packages also include a third smart port for monitoring/shutdown via EIA 232 and is compatible with OnliNet software but not compatible with basic software included in kit.

### PowerMon Basic Monitoring Software

PowerMon software is a software interface that allows the UPS to communicate with most operating systems. Upon power loss, PowerMon will perform an unattended automatic system shutdown at a user-defined time or upon receipt of a low battery signal from the UPS system. It also keeps a record of power outages with history graph.

PowerMon operates as a background task and continually polls the UPS via its EIA-232 or LAN relay port and communicates to the EIA-232 port of the CPU. When power fails, a countdown timer (user-defined) is activated and a message “on battery backup” is broadcast to all users on the system. A final “system shutdown” message will appear prior to automatic power down. PowerMon has four user-modifiable scripts and an outpaging function that can be activated during power loss to execute functions toward an orderly system shutdown. Note: PowerMon requires a dedicated asynchronous EIA-232 port that supports modem control to detect low battery signal. See software ordering chart.

### OnliNet and OnliSafe for Prestige and PUPS Plus On-line UPS Systems

OnliNet requires a UPS with an EIA 232 port.

OnliNet Basic:  Full power monitoring in addition to basic “single CPU” shutdown, user friendly graphic interface allows remote tests and diagnostics:

OnliNet Network:  Same as OnliNet basic except multiple CPU shutdown and Network power management provisions.

OnliSafe:  Basic CPU shutdown with same features as PowerMon noted above; works with LAN relay or asynchronous EIA232 port.

### Software Ordering Chart for UPS Systems

Part numbers noted OnliSafe and PowerMon are CPU shutdown with limited monitoring and notification. Part numbers noted OnliNet are full graphics display and extended UPS monitoring. Where noted Onlinet V3.1 also provides waveform display, simultaneous monitoring of remote adapters, battery test, built-in SNMP communications & integrated with Netview and Openview.

|  | One-UPS1 | Prestige Models | PUPS-Plus Models | Matrix | HA3000/HA4000 (EPE) |
| --- | --- | --- | --- | --- | --- |
| SUN-OS Sparc, CD-ROM | 4N-AEAES-CC OnliSafe | 4N-AEAES-AD/BD OnliNet V3.12 | 4N-AEAES-AD/BD OnliNet V3.12 | N/A | 4N-JBBBB-AF PowerMon |
| SUN-Solaris Workstation UNIX, CD-ROM | 4N-AEAES-CC OnliSafe | 4N-AEAES-AD/BD OnliNet V3.12 | 4N-AEAES-AD/BD OnliNet V3.12 | N/A | N/A |
| SUN-Solaris x86 PC UNIX, 3.5” | 4N-AEAES-CG OnliSafe | 4N-JBBBB-AG PowerMon | 4N-JBBBB-AE PowerMon | N/A | 4N-JBBBB-AF PowerMon |
| IBM-AIX, 3.5” | 4N-AEAES-CC OnliSafe | 4N-AEAES-AC/BC OnliNet2 | 4N-AEAES-AC/BC OnliNet V3.12 | N/A | 4N-JBBBB-AF PowerMon |
| HP-UX, CD-ROM | 4N-AEAES-CC OnliSafe | 4N-AEAES-AE/BE OnliNet2 | 4N-AEAES-AE/BE OnliNet V3.12 | N/A | N/A |
| SCO Unix, 3.5” | 4N-AEAES-CG OnliSafe | 4N-AEAES-AG/BG OnliNet2 | 4N-AEAES-AG/BG OnliNet2 | N/A | 4N-JBBBB-AF PowerMon |
| Digital Ultrix | 4N-AEAES-CL OnliSafe | 4N-AEAES-EL OnliSafe | 4N-AEAES- OnliSafe | 4N-JBBBB-CB PowerMon | 4N-JBBBB-CF PowerMon |
| Tru64 UNIX, CD-ROM | 4N-AEAES-CD OnliSafe | 4N-AEAES-AK/BK OnliNet | 4N-AEAES-AK/BK OnliNet | N/A | 4N-JBBBB-FF PowerMon |
| Alpha & VAX OpenVMS, CD-ROM | 4N-AEAES-CM OnliSafe | 4N-AEAES-EM OnliSafe | 4N-AEAES-FM OnliSafe | 4N-JBBBB-GB PowerMon | 4N-JBBBB-GF PowerMon |
| Alpha & VAX OpenVMS, TK50 V5.1 or later | 4N-AEAES-CE OnliSafe | 4N-AEAES-EE OnliSafe | 4N-AEAES-FE OnliSafe | 4N-JBBBB-DB PowerMon | 4N-JBBBB-DF PowerMon |
| VAX OpenVMS, Magtape V5.1 or later | 4N-JBBBB-EA PowerMon | 4N-JBBBB-EG PowerMon | 4N-JBBBB-EE PowerMon | 4N-JBBBB-EB PowerMon | 4N-JBBBB-EF PowerMon |
| Windows NT Alpha, CD-ROM | N/A | 4N-AEAES-AA/BA OnliNet2 | 4N-AEAES-AA/BA OnliNet2 | N/A | N/A |
| Windows NT x86, 3.5” | N/A | 4N-AEAES-AB/BB OnliNet2 | 4N-AEAES-AB/BB OnliNet2 | N/A | N/A |
| Windows DOS, 3.5” | N/A | 4N-AEAES-AH OnliNet | 4N-AEAES-AH OnliNet | N/A | N/A |
| OS/2, 3.5” | 4N-AEAES- OnliSafe | 4N-AEAES-AJ OnliNet | 4N-AEAES-AJ OnliNet | N/A | N/A |
| Novell V2.0 or later Netware V3.11 or later | 4N-AEAES-CF OnliSafe | 4N-AEAES-BF OnliNet3 | 4N-AEAES-BF OnliNet2 | N/A |  |

1.	All models except 250 VA One-UPS.

2.	Part numbers shown for OnliNet Basic/Network Power Management Software available for these operating systems. OnliNet Network allows single point management and multi-CPU shutdown interface via network adapters.

3.	Novel NVX OnliNet Network Software allows network management of other UPS systems on the network. Not compatible with network adapters.

### UPS and Options Quick Selector

| System | Input Plug | UPS System | Receptacle Module | Software | Est. Max. Load (VA) w/Monitor |
| --- | --- | --- | --- | --- | --- |
| AlphaServer 8400 (3-phase), 7000 | (2) L21-30 | 4N-AEAAN-BA | 4N-AEACM-BK | (2) | 4600++ |
| AlphaServer 8400 (1-phase) | (2) L6-30P | 4N-AEAAL-DA | 4N-AEACK-DN | (2) | 4600++ |
| AlphaServer 8200 (1-phase) | (2) L6-30P | 4N-AEAAJ-CL | Included | (1) | 2600++ |
| AlphaServer 8200 Cab System/w storage | (2) L6-20P | 4N-AEAAJ-CS | Included | (1) | 3600++ |
| AlphaServer 8400 Cab System/w storage | (1) L6-20P/30P | 4N-AEAAL-DA | 4N-AEACK-DN | (2) | 5600++ |
| AlphaServer 82/8400 (1-phase) w/SW500 | (2) L6-30/L5-30 | 4N-AEAAL-DA | 4N-AEACK-DN | (2) | 4520/6520 |
| AlphaServer 82/8400 (1-phase) w/SW800 | (2) L6-30/L21-30 | 4N-AEAAN-BA | 4N-AEACM-BN | (2) | 7400/9400 |
| AlphaServer 82/8400 (3-phase) w/SW800 | (4) L21-30 | 4N-AEAAN-BA |  | (2) | 7400/9400 |
| AlphaServer 2100, AlphaServer 4100 |  | 4N-AEAAH-AM | Included | (1) | 1540++ |
| AlphaServer 2100 Cab (240V) | (2) L6-20P | 4N-AEAAJ-CS | Included | (1) | 3780++ |
| AlphaServer 2100 Cab (120V) | (2) L6-30P | 4N-AEAAJ-CM | Included | (1) | 3780++ |
| AlphaServer 2000 |  | 4N-AEABG-AF | Included | (1) | 1270++ |
| AlphaServer 1000/AlphaStation 600 |  | 4N-AEABF-AA | Included | (1) | 945 |
| AlphaServer 1000/AlphaStation 600 Cab System |  | 4N-AEABF-CA | Included | (1) | 1125 |
| AlphaServer/AlphaStation 400 and XL |  | 4N-AEABD-AF | Included | (1) | 725 |
| MicroVAX 3100, VAX 4000-100, AlphaStation 200/250 |  | 4N-AEABC-AF | Included | (1) | 470 |
| VAX 4000/200-700 |  | 4N-AEABF-AB | Included | (1) | 1340 |
| AlphaServer 2100LP Cab (1-4 Systems) | (2) L5-30P | 4N-AEAAJ-CM1 | Included | (1) | 3240++ |
| AlphaServer 2100LP Cab (5-8 Systems) | (4) L5-30P | 4N-AEAAN-BA | 4N-AEACK-BC | (2) | 6480++ |
| AlphaServer 4100 Cab (3 Systems) | (1) L6-30P | 4N-AEAAJ-CL2 | Included | (1) | 3600++ |
| AlphaServer 4100 Cab. (4+ Systems) | (1) L6-30P | 4N-AEAAL-DA | 4N-AEACK-DN | (2) | 4800++ |
| VAX 4000/100 Cab (2 Systems + storage) | (2) L5-30P | 4N-AEACH-AM3 | 4N-AEACH-AC | (1) | 2350 |
| VAX 4000/200-700 Cab (1 System + 2 BA350) | (2) L5-30P | 4N-AEACH-AM3 | 4N-AEACH-AC | (1) | 1700 |
| VAX 4000/200-700 Cab (2 Systems + 6 BA350) | (2) L5-30P | 4N-AEAAJ-AM | Included |  | 3760 |
| VAXstation 4000 60/90 |  | 4N-AEABD-AF | Included | (1) | 640 |
| AlphaStation 255 |  | 4N-AEABC-AF | Included | (1) | 575 |
| AlphaStation 500 |  | 4N-AEABE-AF | Included | (1) | 775 |

1.	Cabinet mount UPS also available

2.	Loads are for fully configured system and include video monitor. External devices may require larger UPS

### Companion Data and AC Power Surge Protection

See UPS Options and TVSS Section also

| Modem | 10BaseT | ThinWire | Multi-port | AC Power 3 Stage | AC Power 5 Stage Hybrid High Performance |
| --- | --- | --- | --- | --- | --- |
| 4N-GA249-AB* | 4N-GA249-CA* | 4N-GA510-B | 4N-GA245-xx | 4N-GA350-DA* | 4N-GA430-AF* |
| wall plug-in | wall plug-in | device port | din rail/rackmount | 3 receptacle strip | 3 receptacle strip |

*	Additional plug-in data modules, 4N-GA240-xx for 4N-GA249/4N-GA350/4N-GA420 series devices. AC panel protection aslo available, All devices include 5 year hot-swap warranty.

### UPS Monitoring/Power Management Software

|  | Windows NT Alpha/Intel | Tru64 UNIX | Alpha and VAX OpenVMS EM/FM=CD-ROM, EE/FE=TK50 |
| --- | --- | --- | --- |
| Basic Monitoring | 1 | 4N-AEAES-AA/AB | 4N-AEAES-AK | 4N-AEAES-EM/EE |
| and | 2 | 4N-AEAES-AA/AB | 4N-AEAES-AK | 4N-AEAES-FM/FE |
| Safe Shutdown |  |  |  | 4N-JBBBB-GB |
| Internetworking or Multi-Shutdown 2 | 1, 2 | 4N-AEAES-BA/BB | 4N-AEAES-BK | See chart below |
| Network Adapter for SNMP | 1, 2 | Network adapter 4N-AEAEO-DA/DC, twisted pair/ThinWire (120V) |

### Basic Monitoring & Shutdown for Multiple Systems on 1 UPS

Packages include PowerMon software, cables and adapters for Alpha Windows NT, Tru64 UNIX, Standard UNIX, OpenVMS and Novell.

| Up to 8 ports | Up to 4 ports | Up to 2 ports* |
| --- | --- | --- |
| 4N-JMIU8-AA | 4N-JMIU4-AA 4N-JMIU4-AB (hardware only) | 4N-JMMCR-AA |

*	Includes third port for network monitoring; not compatible with PowerMon software.

Note:	See UPS Options Section for more details on available options.

### Custom Configuration and System Load Information

Step 1—Determine Load Requirements

Determine present load requirements by adding VA and Watts components of CPU cabinet, external expansion, video console, and other equipment to be supported by UPS. Use the chart below for VA values and multiply by 0.7 for watts unless noted (see footnote 1) as power factor corrected, VA=Watts. CPU cabinet and storage loads are for maximum internal devices and, unless noted, do not include video monitor.

Determine future load potential by adding load requirement of any planned free-standing equipment.

Note:	Desktop UPS systems should not be used to support laser printers, large line printers, or RA/TA/TU devices.

### Single-Phase Systems and Storage Estimated Load Ratings

| Systems | Estimated Load (Volt-Amps) without monitors5 unless noted** | Special Receptacle (all others (1) 5-15R) |
| --- | --- | --- |
| AlphaServer 8400 Rackmount | 46001 | L6-30R & L6-20R |
| AlphaServer 8200 Rackmount | 26001 | (2) L6-20R |
| AlphaServer 4100 Rackmount | 1100 each system1 | IEC320 in cab5 |
| AlphaServer 4100 and 2100 Pedestal (1 ps/2 ps) | 880/12801 | (1) 5-15R/ (2) 5-15R |
| AlphaServer 2100 Rackmount | 1200 each system1 | (2) 5-15R in cab5 |
| AlphaServer 2100LP Rackmount | 810 each system1 |  |
| AlphaServer 20001 (1 ps/2 ps) | 700/10201 | (1) 5-15R/ (2) 5-15R |
| AlphaServer 1000, AlphaStation 600 (1 ps/2 ps) | 745/745 | (1) 5-15R/ (2) 5-15R |
| AlphaStation 500 | 625 |  |
| AlphaStation/ AlphaServer 400 | 575 |  |
| AlphaStation 255 | 375 |  |
| AlphaStation 200/250 | 320 |  |
| VAX/DEC 7000 Rackmount (1 sys w/storage) | 45001 | (2) L6-30R |
| VAX/DEC 7000 Rackmount (2 sys w/o external storage) | 40001 | (2) L6-30R |
| DEC 4000 Model 600/7001 | 1740 VA1 | (1) 5-20R |
| DEC 3000 Model 500/800 | 935 VA |  |
| DEC 3000 Model 400/600 | 800 VA |  |
| DEC 3000 Model 300X/300LX | 380 VA |  |

### Single-Phase Systems and Storage Estimated Load Ratings (continued)

| Systems | Estimated Load (Volt-Amps) without monitors5 unless noted** | Special Receptacle (all others (1) 5-15R) |
| --- | --- | --- |
| DEC 2000 Model 300 | 375 VA |  |
| DEC 2000 Model 500 | 1230 VA (includes two power supplies, requires one 5-15R receptacle) |
| VAX 4000 Model 200-700 | 1140 VA |  |
| VAX 4000 Model 100A | 250 VA |  |
| MicroVAX/VAXstation 3100 | 250 VA |  |
| MicroVAX 3300 | 530 VA |  |
| MicroVAX 3400/3500/3800 | 1030 VA |  |
| MicroVAX 3600/3900 | 2880 VA | (1) L5-30R |
| MicroVAX II (BA23) | 400 VA |  |
| MicroVAX II (BA123) | 800 VA |  |
| VAXft 110 (2 CPU power supplies) | 928 VA (total) | (2) 5-15R |
| VAXft 810 (dual-cabinet system) | 3000 VA/2400 W per system zone4 | (1) L5-30R and (1) 5-20R per zone |
| VAXstation 4000 Model 60/90 | 357 VA |  |
| VAXstation VLC | 100 VA |  |
| DECsystem 5900 | 1630 VA | (1) L5-30R |
| DECsystem 5400/5500 | 855 VA |  |
| DECsystem 5100 | 480 VA |  |
| DECsystem/DECstation 5000 | 300 VA |  |
| DECsystem 3100/DECstation 2100 | 250 VA |  |
| VXT 2000/2000+ | 300 VA** |  |
| applicationDEC 433MP | 990 VA** |  |
| applicationDEC 433XP | 700 VA** |  |
| DECpc AXP 150 | 575 VA** |  |
| DECpc (deskside 4xx-MT/ST) | 575 VA** |  |
| DECpc XL models | 700 VA** |  |
| Venturis FP 4xx, DECpc Lpx | 330** |  |
| Venturis LP 4xx/560, DECpc Lpv | 250** |  |
| Expansion Boxes/CD-ROM (one cabinet) | Estimated Load | Special Receptacle (other than 5-15L) |
| BA350/355/356 w/BA35X-HA/HD power supply | 250 VA w/BA35X-HA/HD 200 VA1 w/BA356-HF | Up to (2) 5-15R for redundant power supply |
| BA346 Pedestal | 410 VA | Up to (2) 5-15R for redundant power supply |
| BA347 Pedestal | 270 VA1 |  |
| BA362 | 390 VA | Up to (2) 5-15R |
| BA364 | 600 VA | Up to (2) 5-15R |
| RAID Array 110/210 w/(2) BA35X-HA | 375 VA w/BA35X-HA 270 VA1 w/BA35X-HF | Up to (4) 5-15R |
| BA353 | 150 VA |  |
| B400X, R400X | 1140 VA |  |
| SZ12, PCXAR-xx | 300 VA |  |
| SZ18 | 200 VA |  |
| SZ16 | 570 VA |  |
| Other Storage Devices |
| MD410 | 180 VA |  |
| RRD42x | 60 VA |  |
| RRD40, RW504/51, TK50Z-GA, TLZ08/09 | 200 VA |  |
| RW100/514/516 | 330 VA |  |
| RF72B/31B/30B/73B/R215F | 520 VA |  |
| SA/SF/SZ100, SF35 | 430 VA |  |
| SA/SF 300 | 2520 VA | (1) L5-30R |
| TF, TA, TZ85/86, TLZ06/04 | 100 VA |  |
| TF, TA, TZ857/867 | 160 VA |  |

### Single-Phase Systems and Storage Estimated Load Ratings (continued)

| Systems | Estimated Load (Volt-Amps) without monitors5 unless noted** | Special Receptacle (all others (1) 5-15R) |
| --- | --- | --- |
| SF7x | 250 VA |  |
| RA8X 3-high cabinet | 2500 VA | (1) L5-30R |
| RA9X 3-high cabinet | 2200 VA | (1) L5-30R |
| SW300 | 1440 VA |  |
| SW500 | 1200 VA | L5-20R3 |
| Printers |
| LA50/70/75/95/LJ2x | 70 VA |  |
| LA120/324/424 | 190 VA |  |
| LA210/310 | 230 VA |  |
| LG01/02 | 960 VA |  |
| LG31/06/12 | 500 VA |  |
| LP29 | 1460 VA | (1) L5-30R |
| LP37 | 1000 VA |  |
| LJ16P | 35 VA |  |
| LJ32P | 60 VA |  |
| LPS20/322 | 1400 VA |  |
| LPS172 | 300 VA |  |
| LN032 | 1200 VA | 5-15R or 5-20R |
| Video Monitors/Terminals | Estimated Load | Special Receptacle (other than 5-15L) |
| VRT19, VR299 | 260 VA |  |
| VR319/320, VR297 | 200 VA |  |
| VRM17 | 100 VA |  |
| VT220/VT420 | 80 VA |  |
| VT320 | 60 VA |  |
| Decservers/Routers |
| DEChub 90 (DEHUB) | 240 VA |  |
| DECserver 90L (DSRVD) | 100 VA |  |
| DECserver 90L (DSRVG), 100, 200, 250, DELNI | 40 VA |  |
| DECserver 300, 700, 900 | 120 VA |  |
| DECserver 500/550 | 1140 VA |  |
| InfoServer 100, 150 | 350 VA |  |
| DEChub 900 (DMHUB) | 650 VA |  |
| HSC60/65/90 | 1400 VA | (1) L5-30R |

### Three-Phase Systems and Storage Estimated Load Ratings

| Systems | Estimated Load | Special Receptacle |
| --- | --- | --- |
| DEC 7000/VAX 70001 | 5200 VA2 max (2400VA typical) | L21-30R |
| VAX 6000 | 2800 VA | L21-20R |
| Expansion Boxes (one cabinet) |
| VAX/DEC 7000 expansion1 (H9F00) | 4300 VA | L21-30R |
| VAX 6000 expansion (H9657) | 4300 VA | L21-20R |
| Other Storage Devices |
| SF200/SF210 | 1870 VA | L21-30R |
| SF220 | 2840 VA | L21-30R |
| SF400 | 4200 VA | L21-30R3 |
| SF500 | 3100 VA | L21-30R |
| SA600/SA800 | 3300 VA | L21-30R |
| SA900 | 4000 VA | L21-30R |
| SA482 | 3400 VA | L21-30R |
| SW800 | 4800 VA | L21-30R3 |
| RA8X 4-high cabinet | 3400 VA | L21-30R |

1.	For these systems, wattage and VA are approximately equal. Do not exceed UPS maximum wattage or rating

2.	UPS for laser printers must be oversized to handle surge currents; call for information

3.	Two receptacles required for optional redundant power controller

4.	These systems include power factor corrected CPUs and non-power factor corrected storage devices

5.	Rackmount systems generally plug into power controller in cabinet which requires L5-30R, L6-20R, L6-30R; call for information

Step 2—UPS Selection and Battery Time

For custom loads from Step 1, select UPS system based on total VA and wattage load, voltage and phase of equipment, receptacle quantity/type, and battery time. To allow for growth, multiply loads by 1.25 and select UPS with closest rating. See UPS Systems Overview at beginning of chapter for guidelines.

Compar battery time required with that shown in the individual product sections.  Additional support time may require add-on battery or larger UPS selection.

Notes:

1. General-purpose outlets are simplex for desktop systems and duplex for  PUPS Plus. Maximum rating of 15 A and 20 A simplex or duplex receptacles is 1440 VA and 1920 VA, respectively.

2. UPS systems have two ratings: VA (or kVA) and watts (or kW), typically  60–70% of VA (or kVA). This ratio meets all product requirements but may not  meet the requirement for power factor corrected devices. These devices are  noted in the equipment list in Step 1. Do not exceed maximum wattage or VA  rating of UPS.

Step 3—Software for Unattended Orderly CPU Shutdown

Select software order number for associated UPS product and operating system from the software section. Also see UPS Options and TVSS section.

### On-line UPS Systems

| Desktop Servers/Workstations | Midrange-High End Servers | High End Servers |
| --- | --- | --- |
| Prestige Desktop/Rackmount 650-2000VA/1500 & 3000VA | Prestige Series 3000/6000 2500-6000VA | Profile/Plus Models 10-36kVA |

Made for Compaq by Exide Electronics, Compaq’s portfolio of On-line UPS Systems provide premium power-line conditioning and outage protection for critical applications. This type of UPS completely isolates the load from the utility through a double conversion true on-line design and continuously controls the output voltage and frequency output to the computer system within tight tolerances to ensure the highest degree of system availability. A static bypass allows the system to continue to support the load even during overload or electronics failure. Because of the tight regulation they provide, without switching to battery, these microprocessor based on-line UPS systems are the recommended choice for critical “raid-like” applications, areas with very poor voltage stability and standby generator supported applications.

All units feature an intelligent communications interface for full monitoring and control across the network in most operating platform environments. Options include OnliNet/OnliSafe Software for monitoring and safe shutdown, and network adapters for twisted pair and ThinWire connections.

The Prestige models feature a revolutionary third generation on-line design with the industry’s widest voltage input tolerance and a cell-saver feature to offer the most robust protection and battery life available. Units are rackmountable up to 3kVA via rackmount kits and special “rack ready” units are available in 1500 and 3000VA models. All Prestige models include a 3 year hot swap warranty.

### Prestige Desktop UPS Systems

The Desktop Prestige models are positioned for high-end workstations and low end servers. The system features upgradeability, full LED display with meters and alarms, touch panel controls, auto self test and network power management provisions through OnliNet Software.

A surge protected hot swap bypass option which mounts on the rear of models 1800VA and below allows the UPS electronics to be safely swapped out for replacement without impacting the critical load. This option also expands the number of output receptacles available for plug-in connection and includes one receptacle off UPS to surge protect devices which are generally too much for a small UPS to handle, i.e., laser printers.

As a bonus, on-line input power factor correction enables the 2kVA unit to be plugged into a standard NEMA 5-20P wall outlet without being derated. EXT models feature the ability to add plug and play battery extensions to increase support time to over two hours. Rackmount kits are available to mount up to two or three Prestige units or a unit in combination with an extended battery cabinet.

The following models are available:

- Prestige Standard	600-1000VA

- Prestige EXT		1000-1500VA

- Prestige Rackmount	1500 & 3000VA

Prestige Desktop UPS Ordering Information

| Prestige Desktop UPS | 120V Models 50/60Hz | 230V Models 50/60Hz | Capacity VA/ Watts | Runtime (min.) Full/Half load | Receptacle Number 120V/230V |
| --- | --- | --- | --- | --- | --- |
| Prestige 600 | NA | 4N-AEABC-BF | 600/420 | 15 / 30 | (3 )IEC320 |
| Prestige 650 | 4N-AEABC-AF | N/A | 650 / 455 | 15 / 30 | (4 )5-15R/(3) IEC320 |
| Prestige 800 | 4N-AEABD-AF | 4N-AEABD-BF | 800 / 560 | 11 / 20 | (4 )5-15R/(3) IEC320 |
| Prestige 1000 | 4N-AEABE-AF | 4N-AEABE-BF | 1000 / 700 | 7 / 14 | (4 )5-15R(3) IEC320 |

### Prestige Desktop UPS Systems (continued)

| Extended Run Models (Upgradeable to 1500VA; add up to 4 battery packs - mix of full or half packs) - see Runtime chart below |
| --- |
| Prestige 800 EXT | N/A | 4N-AEABD-BG | 800/560 | 11 / 20 | (3 )IEC320 |
| Prestige 1000 EXT | 4N-AEABE-AG | 4N-AEABD-BG | 1000 / 700 | 10 / 20 | (4 )5-15R(3) IEC320 |
| Prestige 1250 EXT | 4N-AEABF-AA | 4N-AEABE-BG | 1250 / 900 | 9 / 17 | (4 )5-15R(3) IEC320 |
| Prestige 1500 EXT | 4N-AEABF-AB | 4N-AEABF-BF | 1500 / 1000 | 8 / 18 | (4 )5-15R(3) IEC320 |
| Prestige 1800 EXT | N/A | 4N-AEABF-BH | 1800/1200 | 5/12 | (3 )IEC320 |
| Prestige 2000 EXT | 4N-AEABG-AF | See Series 3000 2.5kVA model | 2000 / 1300 | 4 / 10 | (4 )5-15R / (1) 5-20 |
| Extended Run Pkgs |
| Prestige 2000 EXT |  |  |  |  |  |
| w/ full pack | 4N-AEABG-AG | See Series 3000 | 2000/1300 | 14 / 40 | (4) 5-15R |
| w/ half pack | 4N-AEABG-AH | See Series 3000 | 2000/1300 | 7 / 20 | (4) 5-15R |
| Battery Packs for EXT models |
| Add-on half battery pack | 4N-AEABF-BA | 4N-AEABF-BC | N/A | see run time chart | N/A |
| Add-on full battery pack | 4N-AEABF-BB | 4N-AEABF-BD | N/A | see run time chart | N/A |
| Rackmount Units |
| Prestige 1500EXT | 4N-AEABF-CA | N/A | 1500/1050 | 7/20 & 14/401 | (4) 5-15R |
| Prestige 3000EXT w/L6-30P | N/A | 4N-AEAAH-DA | 3000/2100 | 7/20 | (1) IEC320 C19, 16A |
| Prestige 3000EXT w/IEC309 | N/A | 4N-AEAAH-DB | 3000/2100 | 7/20 | (1) IEC320 C19, 16A |
| Add on battery tray1 | 4N-AEABF-BE | N/A | N/A | 14/40 for 1500EXT | N/A |

1	Rackmount units include up to (2) customer front-accessible hot swappable battery trays. 1500EXT unit includes one tray, 3000EXT includes two trays.

2	All 230V units include (2)  IEC 320 output jumpers for load connection

See Software Section for Monitoring/Shutdown Software and Options Section for network adapters, hot swap-out options and rackmount kits

### Prestige EXT Model Run Time Chart in Minutes*

| # of Battery Packs | Run Times @ | 1 = Full Pack 1/2 = Half Pack | STD Unit | STD +1/2 | STD +1 | STD +1 1/2 | STD +2 | STD +2 1/2 | STD +3 | STD +3 1/2 | STD +4 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 800 EXT (230V only) | 560 Watts | @Full Load @Half Load | 13 31 | 27 53 | 55 107 | 83 161 | 111 215 | 139 268 | 167 322 | 192 376 | 220 430 |
| 1000 EXT | 700 Watts | @Full load | 10 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 |
|  |  | @Half load | 25 | 45 | 90 | 140 | 180 | 225 | 265 | 310 | 355 |
| 1250 EXT | 900 Watts | @Full load | 7 | 15 | 30 | 45 | 60 | 75 | 90 | 105 | 120 |
|  |  | @Half load | 20 | 35 | 70 | 105 | 140 | 175 | 210 | 245 | 280 |
| 1500 EXT | 1000 Watts | @Full load | 6 | 14 | 28 | 42 | 57 | 71 | 85 | 100 | 112 |
|  |  | @Half load | 16 | 30 | 60 | 90 | 120 | 150 | 180 | 210 | 240 |
| 1800 EXT | 1000 Watts | @Full load | 5 | 10 | 20 | 28 | 40 | 50 | 60 | 70 | 80 |
| (230V only) |  | @Half load | 13 | 27 | 55 | 83 | 111 | 139 | 167 | 192 | 220 |
| 2000 EXT | 1300 Watts | @Full load | 4 | 7 | 14 | 21 | 28 | 35 | 42 | 49 | 66 |
| (120V only) |  | @Half load | 10 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 |

*	Run times based on typical computer type load @ 0.65 PF

### Prestige Desktop Systems Specifications

| Models6 | Standard | EXT | Rackmount |
| --- | --- | --- | --- |
| 120V Models | 650 | 800 | 1000 | 1000 EXT | 1250 EXT | 1500 EXT | 2000 EXT | 1500 EXT |
| 230V Models | 600 | 800 | 1000 | 800 EXT | 1000 EXT | 1250 EXT | 1500 EXT | 3000 EXT |
| System Input Characteristics |
| Input voltage range 120V without using battery 230V | 85-144 VAC (Full Load) 75-144 VAC (Half Load) 140-276VAC |
| Max amps continuous 120/230V | 4.8/2.6 | 5.6/3.1 | 7.1/3.9 | 7.1/3.1 | 8.85/3.9 | 10.6/4.8 | 14.2/5.8 | 10.6/12.5 |
| Input frequency | 45-65 Hz |
| Input Cord 120V Models 230V Models | 6 ft (2m) detachable with standard plug 5-15P IEC320 C19 (16A) male connector | 5-20P | 5-15P L6-30P, IEC309 |
| Input power factor | .95 (120V models) and .90 (240V models) @ full load |
| System Output Characteristics |
| Output voltage | 120 Vac (North American models); 208/220/230/240V selectable (International models) ±3 |
| 120V Models VA/Watts | 650/455 | 800/560 | 1000/700 | 1000/700 | 1250/900 | 1500/1000 | 2000/1300 | 1500/1050 |
| 230V Models VA/Watts | 600/420 | 800/560 | 1000/700 | 800/560 | 1000/700 | 1250/900 | 1500/1000 | 3000/2100 |
| Amps continuous 120V/230V | 5.4A/2.6A | 6.7A/3.5A | 8.3A/4.3A | 8.3A/3.5A | 10.4A/4.3A | 12A/5.4A | 16A/6.5A | 12A/12A |
| Amps Peak @<5% THD at 3:1 crest factor 120/230V | 16.2/7.8 | 20/10.5 | 25/12.9 | 25/10.5 | 31/12.9 | 35/16.2 | 48/19.5 | 36/36 |
| Output frequency | 50 Hz or 60 Hz1 ±3 Hz2 (±0.1%)3 |
| Receptacles 120 V | (4) 5-15R; (7) with Power Pass option | (4)5-15R (1)5-20R | (4)5-15R |
| Receptacles 230V | (3) IEC320, 10A; (6) with Power Pass option | (1)IEC320 16A & 7A |
| Overload before bypass transfer | (106% to ( 110% 4 min; ( 10% 4 seconds |
| Transient response | ±18% nominal output V. for 100% load Step or drop on battery |
| Noise rejection @ 100 kHz Normal/common mode | 80/60db |
| Environmental Specifications |
| Temperature, humidity, altitude | 10°C to 40°C operation; –20°C to 60°C storage; 5% to 95% noncondensing Operation @4000 ft without derating |
| Btu/hour online 120V/230V | 185/200 | 236/236 | 295/295 | 295/236 | 380/295 | 421/380 | 604/421 | 421/931 |
| Audible noise @ 1 meter | <45 dBA |
| Agency Compliance |
| Surge/electrostatic (ESD) | IEEE 587/ANSI C6 2.41 CAT A&B/ESD withstand 200 kV |
| EMI suppression | EN50081-1, EN50082-1 (230V) FCC Part 15, Subpart J, Class A (120V) |
| Safety | UL 1778, Canadian Standards Assoc. Listed; EN50091-1 |
| Weight and Dimensions UPS System (Including Internal Battery) |
| Weight | 12.9kg (28.5 lb) All | 14.9kg (33 lb) All | 36.6kg(81 lb) 54.5kg(120 b) |
| Dimensions (H x W x D) | 252 x 143 x 400 mm (9.9 x 5.6 x 15.8 inches) | 6.97x17x24 in |
| Extended Battery Pack |
| Weight | N/A | 13.4 kg (29.5 lb) half (each) 23.6 kg (52 lb) full (each) | N/A |
| Dimensions (H x W x D) | N/A | 252 x 143 x 400 mm (9.9 x 5.6 x 15.8 inches | N/A |
| Batteries—sealed lead acid type |
| Recharge Time to 80% | Standard Extended | 4 Hrs (120V Models) N/A | 8 Hrs (230V Models) Call for information | 4 hrs 4 hrs |
| Duration Full/ half load min5 | 120V standard 230V | 15/30 16/30 | 10/24 10/24 | 8/16 8/16 | 10/25 5/13 | 7/20 10/25 | 6/16 7/20 | 4/10 6/16 | 6/16 7/20 |
|  | Extended 120V | N/A | See Runtime Chart | 14/30 |
|  | Extended 230V | N/A | See Runtime Chart | N/A |

1.	Input frequency automatically sensed.

2.	Normal operation; output synchronized to input.

3.	Input frequency out of acceptable limits or input not present.

4.	Recharge time after discharge into 100% load.

5.	Battery time within +-10% based on system wattage and normal ambient temperature.

6.	240 V models include (2) ouput jumpers with IEC320 connection.