About the MSMQ MQIS Update/Restore Wizard

This document supplements the instructions given in the MSMQ MQIS Update/Restore wizard. You should read this document in its entirety before running the MSMQ MQIS Update/Restore wizard.

Introduction

You can run the MSMQ MQIS Update/Restore wizard to restore or to update an MSMQ 1.0 MQIS database. You should restore an MQIS database if an MSMQ 1.0 server (PEC or PSC) has suffered a hardware or software failure. Software failures may include failure or corruption of Windows NT Server, SQL Server, or the MSMQ MQIS database. You must update an MQIS server database if it contains objects that are not synchronized with the restored MQIS server. Typically, you will update the MQIS database on one or more servers in your enterprise after restoring a failed MQIS server.

You must have SQL administrative permissions on every MQIS server in your enterprise for the wizard to successfully function.

But first some definitions:

·	Restore operation: the objective of a restore operation is to create a new MQIS database on a failed server based solely on another MQIS server database.

·	Update operation: the objective of an update is to synchronize an MQIS server database, which is potentially out of date, with another MQIS server.  Note that only an MQIS server that has been restored can provide updating services for another MQIS server.

·	Restored server: an MQIS server that the restore wizard has been successfully run on in restore mode.  Other MQIS servers in the enterprise might need to synchronize (update their MQIS databases) with this restored server.

Overview

The goal of the MQIS restore/update process is to reconstruct coherent MQIS databases throughout an MSMQ enterprise given a failure on some MQIS server.  It is useful to think of the reconstruction as consisting of two required phases:

·	Phase 1: restore a failed MQIS server database.

·	Phase 2: update all other MQIS servers in the enterprise that depend on the restored server.

Note that this reconstruction process is executed for each failed MQIS server in the enterprise.  In other words, if you encounter two failed MQIS servers, F1 and F2, you would first execute the reconstruction procedure for F1.  Once that completed you would execute it again for F2.  In this manner, you ultimately will re-create a valid MSMQ enterprise.

Before You Begin

Several tasks may need to be performed before you can run the MQIS Update/Restore wizard.  These depend on the nature of the software failure:

·	If Windows NT 4.0 Server has failed, you must first reformat the server disks, then reinstall Windows NT Server 4.0 with Service Pack 3, and then reinstall SQL Server 6.5.

·	If SQL Server has failed, you will need to reinstall SQL Server 6.5.

·	If the MQIS database is corrupted (detected by corruption events appearing in the system event log), you will need to remove the MQIS database and MQIS devices (MQISData and MQISLog) from SQL server.

·	Stop the MSMQ service.

·	Next, restart the computer, verify that the MSSQLServer service is running, and confirm that SQL Server is in "mixed-security" mode.

·	Finally, install MQIS Restore Wizard from the Service Pack 4 media. The setup program, MQRSTR.EXE, is located at \support\msmq.nt\i386 (or \support\msmq.nt\alpha).

Restoring an MQIS Database

When you are ready to start the wizard, type mqisrstr from the installation folder.  To restore an MQIS database, click Restore Database, and follow the instructions given in the wizard. You will be prompted to enter the name of an MQIS server to get initial information from. The wizard uses this server to retrieve a list of all the MQIS servers in your enterprise. This can be any MQIS server, as long as it is online, its MSSQLServer service is started, and you have SQL administrative permissions on that server.

Later, you will have the option to select which MQIS server to use in order to restore the failed MQIS server.  You can let the wizard automatically find the most up-to-date server in your enterprise or you can have the wizard use the server you specified previously in Enter the name of an MSMQ MQIS server to get initial information from.

Note: you can only restore the MQIS database with the wizard on a PEC or PSC.  The wizard is not used to reconstruct the MQIS database on a BSC.  If a BSC has failed, you should simply re-install MSMQ on that BSC.  MSMQ will automatically arrange to copy the MQIS database from the appropriate PSC.

If you are restoring your MQIS server due to SQL or MQIS failures, then after the restoration it is sufficient to simply restart the MSMQ service and continue to the update phase.

However, if you are restoring because of an NT failure or a hard disk crash, then once you’ve successfully reinstalled NT, SQL and run the restore wizard, you will of course need to re-install MSMQ itself.  In this case, since the restore process re-created the MQIS database, when MSMQ setup prompts you for the database path, provide the location of the re-created database, and select “re-use existing database”.

Automatically Finding a Server to Restore a Database

Clicking the first option, Yes. I want the wizard to find the best server, may take some time initially but will save you time later. This is the recommended option. The wizard attempts to connect to every MQIS server in your enterprise in order to find the highest sequence number (or SN) of the MQIS server being restored. The server with the highest SN will contain the most up-to-date version of the MQIS database in your enterprise for the server you are attempting to restore. However, there are several reasons the wizard might fail to connect to the best server:

·	You don’t have SQL administrative permissions on the remote server

·	The MSSQLServer service is stopped

·	The MQIS database is full (data or log devices do not have available space)

·	The remote server is offline

·	The communications link to the remote server is very slow

The wizard will skip to the next server after two minutes of attempting to connect. Every such "problematic" server is listed in the failedsrv.ini file located in the folder in which you installed the wizard. You will later need to run the Update option of the wizard on each of these servers. If no failedsrv.ini file is created, then you do not need to run the Update option of the wizard. Here is a sample failedsrv.ini file:

[List of the unreachable servers]

Server1=tanya3nt4

[Information about unreachable servers]

Server1=0xf0f380916c24d21188bc0060081efe1f,2

[Number of the unreachable servers]

Number=1

[Maximal SN]

MaxSN=5

After the wizard has found the most updated MQIS server available (which may or may not be the server with the highest SN), it performs the following tasks:

·	Retrieves the size of the data and log devices from the up-to-date server.

·	Note: If this fails, you must define these sizes manually. Ensure that you have sufficient storage capacity on the failed server that is greater than or equal to the size of the MQIS database on the remote server.

·	Creates a new MQIS database on the failed server

·	Copies the MQIS database from the best server to the failed server

At this point, you have restored the failed MQIS server database. The next step is to reinstall MSMQ server software if needed. You should also renew the cryptographic keys on the restored server. From Control Panel, double-click MS Message Queue, click the Security tab, and then click Renew Cryptographic Keys. Lastly, restart the MSMQ service.

You must rerun the wizard (by clicking Update Database) for each server listed in the "List of the unreachable servers" section of the failedsrv.ini file. This will ensure that all MQIS servers are synchronized with the same information. For more information, see the "Updating an MQIS Database" section later in this document.

Using a Specific Server to Restore a Database

Clicking the second option, No. Just use servername, for restoring an MQIS database, uses the server you specified in Enter the name of an MSMQ MQIS server to get initial information from previously. However, when you choose this option, you must later run the wizard (by clicking Update Database) for each MQIS server in your enterprise.

Note: the failedsrv.ini file will be created in the folder to which you installed the wizard in this case as well.  It will contain the names all MQIS servers in the MSMQ Enterprise except for that being restored.

Updating an MQIS Database

Typically, you will need to update an MQIS database after you have restored another MQIS database in your enterprise.  This is because the version of the MQIS database on the restored server may not match the version of the MQIS database on other MSMQ servers in your enterprise. The servers that need to have their MQIS databases updated will be listed in the "List of the unreachable servers" section of the failedsrv.ini file of the restored server.

To update an MQIS server database, start the wizard, click Update Database, and follow the instructions given in the wizard. The order in which you update the servers is important. The PSC is the first server in each site to be updated. Only once the PSC has been successfully updated should you update the BSCs of this site.

You can run the wizard in Update Database mode from the restored server against all the remote MQIS server listed in the failedsrv.ini file. The wizard automatically updates all server listed in the file. This is the recommended option.

There are several command-line switches and parameters you can specify when running the wizard in Update Database mode:

/u		run wizard in unattended mode.

/i  file path	path to the failedsrv.ini file including filename. This switch is used only when you run in update mode on the restored server: in this case, you will cause all dependent servers listed in failedsrv.ini to update their MQIS databases based on the restored server.

/n sitename	performs update for a server based on the PSC of the site specified.  Note this assumes that this PSC was previously restored.

/r servername	performs update on the specified server

/s	silent - no output to the screen while the wizard runs in unattended mode (default is with output)

Notes:

·	If the sitename parameter is not specified, the wizard updates based on the site the local server belongs to.

·	If the servername parameter is not specified, the wizard updates the local server instead of a remote server. Note that it doesn’t make sense to update an MSMQ server that has been restored itself.

·	The only parameter you can specify in attended mode is the path to the failedsrv.ini file. In that case, the update will be performed on the restored server according to the site of the restored server.

Some examples for running the wizard in Update mode:

mqisrstr /u /i c:\wizard\failedsrv.ini

Runs the wizard in unattended mode, performs the update on each server listed in c:\wizard\failedsrv.ini.  This option is only run on the restored server.

mqisrstr /u /n sitename /r servername

Runs the wizard in unattended mode, performs the update on the server servername according to sitename

mqisrstr /u /n sitename

Runs the wizard in unattended mode, performs update on the local server according to sitename

mqisrstr /u /r servername

Runs the wizard in unattended mode  on the restored server and updates the specified remove server that needs to be synchronized

If you have updated servers listed in the failedsrv.ini file, you can verify that the update operation finished successfully if the “List of the unreachable servers” section of the failedsrv.ini file is empty.