PROVIEW (tm) Integrated System Analyzer and Viewer
       Copyright (C) 1992 - 1993 by McAfee Associates
                    All rights reserved

                     BETA TEST VERSION

              Documentation by Glenn Sullivan


























McAfee Associates            (408) 988-3832 office
3350 Scott Blvd, Bldg. 14    (408) 970-9727 fax
Santa Clara, CA  95054       (408) 988-4004 BBS (25 lines)
U.S.A.                       USR HST/v.32/v.42bis/MNP1-5
                             CompuServe        GO MCAFEE
                             InterNet support@mcafee.COM




Overview

     PROVIEW is a menu driven program used to analyze, view
     and edit the basic components of a system, including the
     system memory, system interrupts, device drivers, and
     installed disk drive sectors and file contents.  PROVIEW 
     will allow you to view system elements in HEX, ASCII or 
     disassembled code format.  Full searching and editing 
     functions are included.

     PROVIEW displays data in real time.  For example, if you are
     viewing a memory location that is being updated by
     the system (the clock interrupt, for example), PROVIEW
     will display the changes as they occur.

Using The Menus

     After you have entered the PROVIEW menu system (type
     PROVIEW at the DOS prompt), you will be able to move
     about the PROVIEW menus to access all of the system
     information. To pull down one of the available menus,
     press the ALT key and the highlighted letter of the
     menu you want or use the mouse to select the pulldown
     list. For example, to access the Memory menu, press
     ALT-M. To access the functions within the pulldown
     list, you can either use the arrow keys to move the
     highlight to the option you want and press ENTER,
     select the option with the mouse, or press the letter
     that is highlighted in that option. For example, in the
     Memory menu to access the list of interrupt vectors,
     press I.

     The PROVIEW menu system allows you to open more than
     one window at a time to view the system parameters.

Using the PROVIEW Windows

     The Window menu contains commands to close, move and
     perform other window-management commands. Most of the
     windows in this program have all the standard window
     elements, including scroll bars, a close box, and zoom
     icons.

     Size/Move  (Ctrl-F5)

          When you choose Size/Move, the active window moves
          in response to the arrow keys. Once you've moved
          the window to where you want it, press Enter.

          If you press Shift while you use the arrow keys,
          you can change the size of the active window. Once
          you've adjusted its size or position, press Enter.

          You can also move a window by dragging its title
          bar with the mouse. If a window has a Resize
          corner, you can drag that corner with the mouse to
          resize the window.


     Zoom  (F5)

          Choose Zoom to resize the active window to the
          maximum size. If the window is already zoomed, you
          can choose this command to restore it to its
          previous size.

          You can also double-click anywhere on the window's
          title bar (except where an icon appears) to zoom
          or unzoom the window.

     Next  (Ctrl-F6)

          Choose Next to cycle forwards through the windows
          on the desktop.

     Close  (Ctrl-F4)

          Choose Close to close the active window.

          You can also click the Close box in the upper
          right corner to close a window.

     Cascade

          Choose Cascade to stack all file viewers on the
          desktop.

           ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ1Ä¿
           ³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ2Ä¿
           ³³ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ3Ä¿
           ³³³ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ4Í»
           ³³³º                         º
           ³³³º                         º
           ³³³º                         º
           ³³³º                         º
           ³³³º                         º
           ÀÀÀÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                  Cascaded Windows



    Tile

          Choose Tile to tile all file viewers on the
          desktop.

           ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
           ³ ÉÍÍÍÍÍÍÍÍÍÍÍÍ1ÍÍ»ÚÄÄÄÄÄÄÄÄÄÄÄÄ2ÄÄ¿ ³
           ³ º               º³               ³ ³
           ³ º               º³               ³ ³
           ³ º               º³               ³ ³
           ³ º               º³               ³ ³
           ³ ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
           ³ ÚÄÄÄÄÄÄÄÄÄÄÄÄ3ÄÄ¿ÚÄÄÄÄÄÄÄÄÄÄÄÄ4ÄÄ¿ ³
           ³ ³               ³³               ³ ³
           ³ ³               ³³               ³ ³
           ³ ³               ³³               ³ ³
           ³ ³               ³³               ³ ³
           ³ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
           ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                       Tiled Windows

Using the Edit Functions

     The Edit menu contains all the commands you need to
     edit or change the system elements that are accessed with
     the Memory and Disk menus.

     Undo  (Backspace)

          To undo any change that you have made. Note that
          any values that have been changed are highlighted.

     Set Mask/Value  (F3)

          The mask/value may be set to any hex byte value for
          XOR/Negate or Add/Subtract operations. 

     XOR/Negate  (F7/Shift-F7)

          XOR/Negate the selected byte using the mask value.

     Add/Subtract (F8/Shift-F8)

          Add/subtract the Mask/Value to the highlighted field.

     Rotate Left/Right  (F9/Shift-F9)

          Rotate selected byte left or right.


Using the PROVIEW Menus

FILE Menu

     The file menu has three options:

     Save Edited Object

          Permits saving any changes you have made without
          having to exit the current edit in process.

     Read only   (Default = No)

          This options allows you to enable or disable the
          Read Only function. When enabled (ON), you will
          not be able to change or edit any system data with
          the PROVIEW program. To make changes, and be able
          to save them, toggle this option to read NO.

     Exit to DOS

          Returns you to the DOS prompt. Be sure to save any
          changes that you have made before exiting.

MEMORY Menu

          System memory may be viewed and edited by PROVIEW.  
          Memory may be viewed in HEX, ASCII or disassembled
          code format.  If viewing in assembler format, you
          may follow the control of the program by selecting
          the numbers in parenthesis to the right of each 
          branch instruction that is displayed on the screen.
          to reverse the flow of control, press (0) to return 
          to the previous branch instruction.

          The following options are available in the Memory Menu:

     DOS System Area

          View/Edit the DOS System Area, starting at 0K and
          taking up as much as space as necessary for all
          the information loaded. Information stored here
          includes the BIOS DATA Area, DOS Communication
          Area, IO and DOS code, System File Tables, FCB
          Tables, Disk Buffers, System STACKS (CODE and
          DATA), as well as devices loaded with the
          CONFIG.SYS file (e.g., HIMEM.SYS, SETVER driver,
          MOUSE driver).

     Program Area

          View/Edit the Program Area, starting at the end of
          the DOS System Area and reserving all needed and
          unused space up to 640K. Information stored here
          includes the COMMAND.COM code, as well as any TSR
          programs loaded by the system (e.g., SMARTDRV,
          DOSKEY).


     Upper Memory Area

          View/Edit the Upper Memory Area, starting at 640K
          and reserving all the needed and unused space up
          to 1MB. Information stored here includes the
          Graphic and Text Video RAM, Video ROM BIOS, and
          System ROM BIOS.

     Interrupts

          View/Edit the List of Interrupts Vectors and
          indicates which ones are currently in use, its
          address and its pointer.

     Drivers

          View/Edit the List of Installed Drivers and
          indicate their address and memory area.

     Absolute Memory View

          View/Edit a user selectable memory address range
          within the system absolute system memory.


                          WARNING!!

          Changes made to system memory can cause system crashes
          or data loss.  Make sure that you understand any change
          that you wish to make to any memory location.


DISK Menu

     File View

          View/Edit files on the default hard disk drive.
          You can view the file in either HEX, ASM or ASCII
          format.

     Sector View

          View/Edit logical sectors on any installed disk
          drive, hard or floppy.

     Physical Sector View

          View/Edit physical sectors on any disk drive.

     Boot Record

          View/Edit the boot record on any installed drive.

     Master Boot Record

          View Edit the Master Boot record on any drive.

                       WARNING!!

          Changes made to the Boot sector, Master Boot Record or
          File allocation table area of the hard disk or floppy disk
          can cause system crashes and/or loss of data.  Make sure
          that you understand any changes made to these areas.





HELP Function

     The help menu displays help on using PROVIEW. Press F1
     to access the help menu and then use the arrow keys to
     move about Help. In the Help Menu is also a section on
     Help On Help. If you are having trouble finding
     anything in Help, or using Help, Press Alt-H to access
     the Help Menu list, the press H to access the Help On
     Help. When you are finished with Help, press Enter or
     select OK with the Mouse to return to the PROVIEW menu.






AUTHENTICITY

               Before using PROVIEW for the first time, verify that it has
          not been tampered with or infected by a virus by using the
          the enclosed VALIDATE program.  For instructions on using
          VALIDATE, please read the VALIDATE.DOC file.

               The validation results for Version BETA should be:

                        FILE NAME: PROVIEW.EXE
                             SIZE: 92,892
                             DATE: 01-22-1993
              FILE AUTHENTICATION
                   Check Method 1: 199F
                   Check Method 2: 1113

          If your copy of PROVIEW differs, it may have been damaged.  Run
          Always obtain your copy of PROVIEW from a known source.  The latest
          version of PROVIEW and validation data for PROVIEW.EXE can be
          obtained from McAfee Associates' bulletin board system at
          (408) 988-4004 or from the McAfee Virus Help Forum on
          CompuServe (GO MCAFEE), or the mcafee.COM anonymous ftp site on
          the Internet.

               PROVIEW series are archived with PKWare's PKZIP Authentic File
          Verification.  If you do not see an "-AV" after every file is
          unzipped and receive the "Authentic Files Verified! # NWN405
          Zip Source: McAFEE ASSOCIATES" message when you unzip the files
          then do not use them.  If your version of PKUNZIP does not have
          verification ability, then this message may not be displayed.
          Please contact us if you believe tampering has occurred to the
          .ZIP file.