| Processor – One of the following: |
| --- |
| Intel Pentium III 600EB MHz |
| Intel Pentium III 733 MHz |
| Intel Pentium III 866 MHz |
| Cache Memory |
| 256-KB Level 2 cache standard |
| Upgradability |
| Upgrades for memory, graphics and hard drives |
| Memory – One of the following: |
| Standard | 128 MB of 712-MHz ECC RDRAM |
| Maximum | 512 MB of ECC RDRAM (1 GB when 288-Mb technology becomes available) |
| Standard | 256 MB of 712-MHz ECC RDRAM |
| Maximum | 512 MB of ECC RDRAM (1 GB when 288-Mb technology becomes available) |
| Network Controller |
| Intel PRO/100+ Management Adapter NIC (10/100 Mb/s Autosensing Ethernet Controller) PCI with Wake-on-LAN and Alert-on-LAN, capable of operating in either 10Base-T or 100 Base-TX environments |
| Expansion Slots |
| I/O (Total/Available) | 7, 5 (4 on SCSI models) |
| Shared PCI/ISA | 1, 1 |
| PCI | 4, up to 3 (depending on SCSI or graphics controller) |
| ISA | 1, 1 |
| AGP | 1, 0 or 1 depending on graphics controller |
| Storage Controllers |
| Integrated UATA/66 on all models |
| Wide Ultra2 SCSI PCI or Ultra3 (Ultra 160) SCSI PCI depending on model (SCSI models only.) |
| Storage |
| Diskette Drives | 1.44 MB |
| CD-ROM | 40X Max CD-ROM Drive (IDE) |
| Hard Drives | One of the following: |
|  | 9.1-GB or 18.2-GB Ultra3 (Ultra 160) SCSI (10,000 rpm) |
|  | 20-GB Ultra ATA/66 (7200 rpm) |
| Interfaces |
| Parallel | 1 |
| USB | 2 |
| Serial | 2 |
| Ultra2 SCSI | 1 (SCSI models only, 50-pin external, 68-pin internal) |
| Keyboard (PS/2) | 1 |
| Pointing Device (PS/2 mouse) | 1 |
| Video | 1 |
| Microphone Jack | 1 |
| Headphone Jack | 1 |
| Line-In Jack | 1 |
| Line-Out Jack | 1 |
| RJ-45 | 1 |
| Graphics – One of the following: |
| 3Dlabs Oxygen GVX1 (AGP) |
| ELSA GLoria II (AGP) |
| ELSA Synergy II (AGP) |
| Matrox Millennium G400 DualHead (AGP) |
| Matrox Millennium G400 (AGP, single display, analog output; digital output available with optional Millennium G400 DVI Daughter Card) |
| Compaq NVIDIA TNT2 Pro (AGP) |
| Matrox G200 Quad Multi-monitor Series (PCI) |
| Audio |
| Compaq Premier(Sound featuring AC’97 Audio |
| Software |
| Compaq Management Agents Compaq PC Diagnostics via the Web ROM-based Setup Compaq Restore CD Microsoft Windows NT Workstation 4.0 or Windows 2000 Professional (depending on model) Diagnostics for Windows NT Microsoft Internet Explorer Microsoft Service Pack 4a System Software Manager via the Web |
| Intelligent Manageability |
| AssetControl Fault Management Security Management Remote Management Remote Wakeup via Magic Packet Support Remote ROM Flash Remote Security Remote Shut Down Pre-Failure Warranty (hard drives, processors and memory) |
| Security |
| Diskette write and boot control Flash ROM lock Keyboard password Network server mode Parallel interface control Power-on password Serial interface control Setup password Cable lock provision |
| Power Supply |
| 200-Watt Power Supply |
| Service and Support |
| Protected by Compaq Services, including a three-year limited warranty with three year parts coverage, three year on-site service, and three year labor; 7 x 24 hardware technical phone support and online support through the Internet; Pre-Failure Warranty coverage of hard drives, processors and memory. |
| Note: Certain restrictions and exclusions apply. Consult the Compaq Customer Support Center for details. Three year onsite and labor not available in all countries. |
|  | Models |
| 25M/866/128R/20A/2 | Processor | Intel Pentium III 866-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 190217-xx1 | Cache Memory | 256-KB L2 | Hard Drive | 20-GB Ultra ATA/66 7200 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Integrated Ultra ATA/66 |
|  | Standard | 128 MB | Graphics | Compaq NVIDIA TNT2 Pro |
|  | Maximum | 512 MB (1 GB when 288-Mb technology becomes available) | Audio OS | AC97 with Compaq Premier(Sound Windows NT Workstation 4.0 |
| 25M/866/128R/20A/2X | Processor | Intel Pentium III 866-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 164494-xx2 | Cache Memory | 256-KB L2 | Hard Drive | 20-GB Ultra ATA/66 7200 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Integrated Ultra ATA/66 |
|  | Standard | 128 MB | Graphics | Matrox Millennium G400 DualHead |
|  | Maximum | 512 MB (1 GB when 288-Mb technology becomes available) | Audio OS | AC97 with Compaq Premier(Sound Windows NT Workstation 4.0 |
| 25M/866/128R/9L/2X | Processor | Intel Pentium III 866-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 164494-xx3 | Cache Memory | 256-KB L2 | Hard Drive | 9.1-GB Ultra3 (Ultra 160) SCSI 10,000 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Wide Ultra2 SCSI |
|  | Standard | 128 MB | Graphics | Matrox Millennium G400 DualHead |
|  | Maximum | 512 MB (1 GB when 288-Mb technology becomes available) | Audio OS | AC97 with Compaq Premier(Sound Windows NT Workstation 4.0 |
| 25M/866/128R/9L/2+ | Processor | Intel Pentium III 866-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 164494-xx4 | Cache Memory | 256-KB L2 | Hard Drive | 9.1-GB Ultra3 (Ultra 160) SCSI 10,000 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Wide Ultra2 SCSI |
|  | Standard | 128 MB | Graphics | ELSA Synergy II |
|  | Maximum | 512 MB (1 GB when 288-Mb technology becomes available) | Audio OS | AC97 with Compaq Premier(Sound Windows NT Workstation 4.0 |
| 25M/866/256R/18L/X | Processor | Intel Pentium III 866-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 190217-xx2 and graphics option | Cache Memory | 256-KB L2 | Hard Drive | 18.2-GB Ultra3 (Ultra 160) SCSI 10,000 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Ultra3 (Ultra 160) SCSI |
|  | Standard Maximum | 256 MB 512 MB (1 GB when 288-Mb technology becomes available) | Graphics | Choice of graphics option: Matrox G200 Quad MMS with analog cables 159513-B21 Matrox G200 Quad MMS with DVI cables 179597-B21 Millennium G400 DualHead 159512-B21 Compaq NVIDIA TNT2 Pro 189998-B21 ELSA Synergy II 103382-B21 ELSA GLoria II 174566-B21 3Dlabs Oxygen GVX1 136398-B21 |
|  |  |  | Audio | AC97 with Compaq Premier(Sound |
|  |  |  | OS | Windows NT Workstation 4.0 |
| 25M/866/128R/9L/X | Processor | Intel Pentium III 866-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 164494-xx5 and graphics option | Cache Memory | 256-KB L2 | Hard Drive | 9.1-GB Ultra3 (Ultra 160) SCSI 10,000 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Wide Ultra2 SCSI |
|  | Standard Maximum | 128 MB 512 MB (1 GB when 288-Mb technology becomes available) | Graphics | Choice of graphics option: Matrox G200 Quad MMS with analog cables 159513-B21 Matrox G200 Quad MMS with DVI cables 179597-B21 Millennium G400 DualHead 159512-B21 Compaq NVIDIA TNT2 Pro 189998-B21 ELSA Synergy II 103382-B21 ELSA GLoria II 174566-B21 3Dlabs Oxygen GVX1 136398-B21 |
|  |  |  | Audio | AC97 with Compaq Premier(Sound |
|  |  |  | OS | Windows NT Workstation 4.0 |
| 25M/866/128R/20A/X | Processor | Intel Pentium III 866-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 164494-xx6 and graphics option | Cache Memory | 256-KB L2 | Hard Drive | 20-GB Ultra ATA/66 7200 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Integrated Ultra ATA/66 |
|  | Standard Maximum | 128 MB 512 MB (1 GB when 288-Mb technology becomes available) | Graphics | Choice of graphics option: Matrox G200 Quad MMS with analog cables 159513-B21 Matrox G200 Quad MMS with DVI cables 179597-B21 Millennium G400 DualHead 159512-B21 Compaq NVIDIA TNT2 Pro 189998-B21 ELSA Synergy II 103382-B21 ELSA GLoria II 174566-B21 3Dlabs Oxygen GVX1 136398-B21 |
|  |  |  | Audio | AC97 with Compaq Premier(Sound |
|  |  |  | OS | Windows NT Workstation 4.0 |
| 25M/866/128R/9L/X/W | Processor | Intel Pentium III 866-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 164494-xx8 and graphics option | Cache Memory | 256-KB L2 | Hard Drive | 9.1-GB Ultra3 (Ultra 160) SCSI 10,000 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Wide Ultra2 SCSI |
|  | Standard Maximum | 128 MB 512 MB (1 GB when 288-Mb technology becomes available) | Graphics | Choice of graphics option: Matrox G200 Quad MMS with analog cables 159513-B21 Matrox G200 Quad MMS with DVI cables 179597-B21 Millennium G400 DualHead 159512-B21 |
|  |  |  | Audio | AC97 with Compaq Premier(Sound |
|  |  |  | OS | Windows 2000 Professional |
| 25M/733/128R/9L/2 | Processor | Intel Pentium III 733-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 388014-xx3 | Cache Memory | 256-KB L2 | Hard Drive | 9.1-GB Ultra3 (Ultra 160) SCSI 10,000 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Wide Ultra2 SCSI |
|  | Standard | 128 MB | Graphics | Matrox Millennium G400 (single) |
|  | Maximum | 512 MB (1 GB when 288-Mb technology becomes available) | Audio | AC97 with Compaq Premier(Sound |
|  |  |  | OS | Windows NT Workstation 4.0 |
| 25M/733/128R/9L/2+ | Processor | Intel Pentium III 733-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 388014-xx4 | Cache Memory | 256-KB L2 | Hard Drive | 9.1-GB Ultra3 (Ultra 160) SCSI 10,000 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Wide Ultra2 SCSI |
|  | Standard | 128 MB | Graphics | ELSA Synergy II |
|  | Maximum | 512 MB (1 GB when 288-Mb technology becomes available) | Audio | AC97 with Compaq Premier(Sound |
|  |  |  | OS | Windows NT Workstation 4.0 |
| 25M/733/128R/9L/3M | Processor | Intel Pentium III 733-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 388014-xx5 | Cache Memory | 256-KB L2 | Hard Drive | 9.1-GB Ultra3 (Ultra 160) SCSI 10,000 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Wide Ultra2 SCSI |
|  | Standard | 128 MB | Graphics | 3Dlabs Oxygen GVX1 |
|  | Maximum | 512 MB (1 GB when 288-Mb technology becomes available) | Audio | AC97 with Compaq Premier(Sound |
|  |  |  | OS | Windows NT Workstation 4.0 |
| 25M/733/128R/9L/X | Processor | Intel Pentium III 733-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 388014-xx7 and graphics option | Cache Memory | 256-KB L2 | Hard Drive | 9.1-GB Ultra3 (Ultra 160) SCSI 10,000 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Wide Ultra2 SCSI |
|  | Standard Maximum | 128 MB 512 MB (1 GB when 288-Mb technology becomes available) | Graphics | Choice of graphics option: Matrox G200 Quad MMS with analog cables 159513-B21 Matrox G200 Quad MMS with DVI cables 179597-B21 Millennium G400 DualHead 159512-B21 Compaq NVIDIA TNT2 Pro 189998-B21 ELSA Synergy II 103382-B21 ELSA GLoria II 174566-B21 3Dlabs Oxygen GVX1 136398-B21 |
|  |  |  | Audio | AC97 with Compaq Premier(Sound |
|  |  |  | OS | Windows NT Workstation 4.0 |
| 25M/600EB/128R/20A/2 | Processor | Intel Pentium III 600EB-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 388014-xx1 | Cache Memory | 256-KB L2 | Hard Drive | 20-GB Ultra ATA/66 7200 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Integrated Ultra ATA/66 |
|  | Standard | 128 MB | Graphics | Matrox Millennium G400 (single) |
|  | Maximum | 512 MB (1 GB when 288-Mb technology becomes available) | Audio | AC97 with Compaq Premier(Sound |
|  |  |  | OS | Windows NT Workstation 4.0 |
| 25M/600EB/128R/20A/2+ | Processor | Intel Pentium III 600EB-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 388014-xx2 | Cache Memory | 256-KB L2 | Hard Drive | 20-GB Ultra ATA/66 7200 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Integrated Ultra ATA/66 |
|  | Standard | 128 MB | Graphics | ELSA Synergy II |
|  | Maximum | 512 MB (1 GB when 288-Mb technology becomes available) | Audio | AC97 with Compaq Premier(Sound |
|  |  |  | OS | Windows NT Workstation 4.0 |
| 25M/600EB/128R/9L/X | Processor | Intel Pentium III 600EB-MHz | Optical Drive | 40X Max CD-ROM Drive |
| 388014-xx6 and graphics option | Cache Memory | 256-KB L2 | Hard Drive | 9.1-GB Ultra3 (Ultra 160) SCSI 10,000 rpm |
|  | Memory | 712-MHz ECC RDRAM | Controller | Wide Ultra2 SCSI |
|  | Standard Maximum | 128 MB 512 MB (1 GB when 288-Mb technology becomes available) | Graphics | Choice of graphics option: Matrox G200 Quad MMS with analog cables 159513-B21 Matrox G200 Quad MMS with DVI cables 179597-B21 Millennium G400 DualHead 159512-B21 Compaq NVIDIA TNT2 Pro 189998-B21 ELSA Synergy II 103382-B21 ELSA GLoria II 174566-B21 3Dlabs Oxygen GVX1 136398-B21 |
|  |  |  | Audio | AC97 with Compaq Premier(Sound |
|  |  |  | OS | Windows NT Workstation 4.0 |
| Country Code Key | XX=00 | North America: English, French |
|  | XX=04 | Europe: German, English |
|  | XX=03 | Europe: English (866-MHz models) |
|  | XX=A4 | Europe: Dutch, French, English |
|  | XX=06 | Europe: Italian, English (600EB and 733-MHz models) |
|  | XX=AH | Europe: Italian, English (866-MHz models) |
|  | XX=B5 | Europe: German, French (866-MHz models) |
|  | XX=07 | Europe: English, Spanish |
|  | XX=29 | Japan: Japanese |
|  | XX=39 | Japan: English |
|  | XX=37 | Asia/Pacific/Greater China: English |
|  | XX=AD | Asia/Pacific: English, Korean (866-MHz models) |
|  | XX=AA | Greater China: English, Simplified Chinese (866-MHz models) |
|  | XX=AB | Greater China: English, Traditional Chinese (866-MHz models) |

| Memory (RDRAM) |
| --- |
| 256-MB Memory Module (800-MHz ECC) | 157341-B21 |
| 128-MB Memory Module (800-MHz ECC) | 157338-B21 |
| 256-MB Memory Module (712-MHz ECC) | 157340-B21 |
| 128-MB Memory Module (712-MHz ECC) | 157337-B21 |
| Monitors |
| TFT8020 Flat Panel Color 18-inch (Opal) | 326100-xxx |
| TFT8020 Flat Panel Color 18-inch (Carbon) | 159244-xxx |
| TFT7000 Flat Panel Color 17-inch (not available in NA) | 136143-xxx |
| TFT5010 Flat Panel Color 15-inch (Opal) | 104741-xxx |
| TFT 5010 Flat Panel Color 15-inch (Carbon) | 154486-xxx |
| P1100 Color CRT 21-inch | 325606-xxx |
| P900 Color CRT 19-inch | 386326-xxx |
| P700 Color CRT 17-inch | 380207-xxx |
| V1100 Color CRT 21-inch | 386472-xxx |
| V710 Color 17-inch | 187895-xxx |
| Note: AssetControl monitor. AssetControl features are accessible with Compaq Workstations featuring Intelligent Manageability. |
| Graphics |  |
| ELSA Synergy II (AGP) | 103382-B21 |
| ELSA GLoria II (AGP) | 174566-B21 |
| Matrox Millennium G400 DualHead (AGP) | 159512-B21 |
| Matrox Millennium G400 DVI Daughter Card (used with G400 single display) | 388557-B21 |
| Compaq NVIDIA TNT2 Pro (AGP) | 189998-B21 |
| Matrox G200 Quad Multi-Monitor Series with cables for analog output (PCI) | 159513-B21 |
| Matrox G200 Quad Multi-Monitor Series with cables for DVI output (PCI) | 179597-B21 |
| Matrox G200 Quad MMS DVI Upgrade Cable Kit | 170840-B21 |
| 3Dlabs Oxygen GVX1 (AGP) | 136398-B21 |
| 3Dlabs Oxygen GVX1 (PCI) | 136397-B21 |
| Diskette Drives |
| 250-MB ATAPI ZIP | 294416-B21 |
| 100-MB ATAPI ZIP | 294402-B21 |
| Hard Drives |
| Ultra3 (Ultra 160) SCSI Drives (Ultra3 or Wide Ultra2 performance depending on controller) |  |
| 36.4-GB Ultra3 (Ultra 160) SCSI (10,000 rpm) | 191189-B21 |
| 18.2-GB Ultra3 (Ultra 160) SCSI (10,000 rpm) | 159764-B21 |
| 9.1-GB Ultra3 (Ultra 160) SCSI (10,000 rpm) | 159763-B21 |
| Ultra ATA Drives |  |
| 20-GB Ultra ATA (7200 rpm) | 124724-B21 |
| 10-GB Ultra ATA (7200 rpm) | 127452-B21 |
| Storage Controllers |
| Compaq Dual-Channel Ultra3 (Ultra 160) SCSI Controller, Adaptec 3960D | 144387-B21 |
| Compaq Single-Channel Ultra3 (Ultra 160) SCSI Controller, Adaptec 29160N | 157810-B21 |
| Wide Ultra2 SCSI Controller, Adaptec 2940UW2 | 124720-B21 |
| Tape Drives |  |
| TR5 10/20-GB | 294243-B21 |
| 12/24-GB DDS-3 DAT | 295513-B21 |
| Biometrics |
| Compaq Fingerprint Identification Technology | 294307-001 |
| Multimedia |  |
| Premier(Sound PS115 Speakers | 133566-xxx |
| Premier(Sound PS330 Speakers | 160992-xx1 |
| 10X DVD-ROM (without MPEG2 decoder) | 294414-B21 |
| 8X/4X/32X CD-RW | 294407-B21 |
| Communications |
| Intel PRO/100+ Management Adapter | 127453-B21 |
| Compaq NC3123 Fast Ethernet NIC PCI 10/100 WOL | 174830-B21 |
| Compaq NC3122 Fast Ethernet NIC PCI Dual 10/100 | 317450-B21 |
| Compaq NC3134: 64 PCI, Dual Base 10/100 WOL | 138603-B21 |
| Compaq NC3135: 10/100 Dual Upgrade Module (for NC3134) | 138604-B21 |
| Compaq NC4621 TR PCI 4/16 WOL | 379956-B21 |
| V.90 PCI Modem (available in North America only) | 171914-001 |
| Uninterruptible Power Systems |
| Compaq Tower UPS Model T1000 (low voltage) | 242688-001 |
| Compaq Tower UPS Model T700 (low voltage) | 295372-B21 |
| Compaq Tower UPS Model T1000h (high voltage, not available in North America) | 242688-002 |
| Compaq Tower UPS Model T700h (high voltage, not available in North America) | 295372-B22 |
| Other |
| Compaq Spaceball 4000 3D Motion Control Input Device | 112138-B21 |
| Compaq Mouse (3 button) | 269192-B22 |
| Compaq Scroll Mouse | 170299-B21 |
| Easy Access Keyboard | 122660-xx6 |
| Compaq Smart Card Keyboard | 115506-xx6 |
| External SCSI Adapter 68-/50-pin | 270187-B21 |
| 12/24-GB DAT Cartridge (10 pack) | 295515-B21 |
| DAT Cleaning Kit | 242781-001 |
| Sliding Shelf Kit for Rack | 332564-B21 |
| Support Software CD |  |
| Annual Subscription | 183426-xxx |
| Single CD-ROM (current month) | 272505-001 |

Compaq Deskpro Workstation AP250 Series with RDRAM (128 MB)

Standard Memory

128-MB RDRAM standard

| Standard | Slot |
| --- | --- |
|  | 1 | 2 |
| 128 MB |  | CRIMM |

Standard Memory Plus Optional Memory

Support for up to 384 MB of RDRAM is available with the installation of optional RDRAM.

| Up To | Slot |
| --- | --- |
|  | 1 | 2 |
| 384 MB |  |  |

Support for up to 640 MB of RDRAM is available with the installation of optional RDRAM when
 288-Mb technology is available.

Standard Memory Replaced 
with Optional Memory

Support for up to 1 GB of RDRAM is available with the removal of the standard 128-MB RIMM and the installation of optional RDRAM when 288-Mb technology is available.

| Up To | Slot |
| --- | --- |
|  | 1 | 2 |
| 512 MB |  |  |
| 1 GB |  |  |

Note:  It is not necessary to add memory in pairs. Memory upgrades are accomplished by adding single or multiple RIMMs of the same or varied sizes. Do not mix memory speeds. These charts do not represent all possible memory configurations.

- 256-MB Memory Kit (RDRAM RIMM, 800 MHz)	157341-B21

- 128-MB Memory Kit (RDRAM RIMM, 800 MHz)	157338-B21

- 256-MB Memory Kit (RDRAM RIMM, 712 MHz)	157340-B21

- 128-MB Memory Kit (RDRAM RIMM, 712 MHz)	157337-B21

Compaq Deskpro Workstation AP250 Series with RDRAM (256 MB)

Standard Memory

256-MB RDRAM standard

| Standard | Slot |
| --- | --- |
|  | 1 | 2 |
| 256 MB |  | CRIMM |

Standard Memory Plus Optional Memory

Support for up to 384 MB of RDRAM is available with the installation of optional RDRAM.

| Up To | Slot |
| --- | --- |
|  | 1 | 2 |
| 384 MB |  |  |
| 512 MB |  |  |

Support for up to 640 MB of RDRAM is available with the installation of optional RDRAM when
 288-Mb technology is available.

Standard Memory Replaced 
with Optional Memory

Support for up to 1 GB of RDRAM is available with the removal of the standard 256-MB RIMM and the installation of optional RDRAM when 288-Mb technology is available.

| Up To | Slot |
| --- | --- |
|  | 1 | 2 |
| 1 GB |  |  |

Note:  It is not necessary to add memory in pairs. Memory upgrades are accomplished by adding single or multiple RIMMs of the same or varied sizes. Do not mix memory speeds. These charts do not represent all possible memory configurations.

- 256-MB Memory Kit (RDRAM RIMM, 800 MHz)	157341-B21

- 128-MB Memory Kit (RDRAM RIMM, 800 MHz)	157338-B21

- 256-MB Memory Kit (RDRAM RIMM, 712 MHz)	157340-B21

128-MB Memory Kit (RDRAM RIMM, 712 MHz)	157337-B21

| Drive Support |
| --- |
|  | Quantity Supported | Position Supported | Controller |
| Removable Media |  |  |  |
| 1.44-MB Diskette Drive | Up to 1 | 1, 2, 3 | Integrated |
| IDE CD-ROM Drive | Up to 1 | 1, 2 | Integrated EIDE |
| 250-MB ATAPI ZIP Drive | Up to 1 | 1, 2 | Integrated EIDE |
| 100-MB ATAPI ZIP Drive | Up to 1 | 1, 2 | Integrated EIDE |
| 8X/4X/32X CD-RW | Up to 1 | 1, 2 | Integrated EIDE |
| 10X DVD-ROM | Up to 1 | 1, 2 | Integrated EIDE |
| Hard Drives |  |  |  |
| Ultra3 (Ultra 160) SCSI Drives (Ultra3 or Wide Ultra2 performance depending on controller) |
| 1-inch 36.4-GB 10,000 rpm 18.2-GB 10,000 rpm 9.1-GB 10,000 rpm | Up to 3 | 1, 2, 3, 4, 5 | Wide Ultra2 SCSI, Adaptec 2940UW2 Compaq Single-Channel Ultra3 (Ultra 160) SCSI, Adaptec 29160N Compaq Dual Channel Ultra3 (Ultra 160) SCSI, Adaptec 3960D |
| Ultra ATA Drives |  |  |  |
| 1-inch 20.0-GB 7200 rpm 10.0-GB 7200 rpm | Up to 3 | 1, 2, 3, 4, 5 | Integrated EIDE |
| Maximum Storage Capacity |
| Internal | 108 GB |
| Tape Drives |  |  |  |
| TR5 10/20-GB | Up to 1 | 1, 2 | Integrated EIDE |
| 12/24-GB DDS-3 DAT | Up to 1 | 1, 2 | Wide Ultra2 or Ultra3 (Ultra 160) SCSI |

| System Unit |  | Tower Dimensions (HxWxD) | 17.65 x 6.6 x 17.11 in/44.83 x 16.76 x 43.46 cm |
| --- | --- | --- | --- |
|  |  | Weight (standard configuration) | 23.7 lbs/10.47 kg |
|  |  | Power Supply |  |
|  |  | Operating Voltage Range | 90 to 132 VAC; 180 to 264 VAC |
|  |  | Rated Voltage Range | 100 to 127 VAC; 200 to 250 VAC |
|  |  | Rated Line Frequency | 50 to 60 Hz |
|  |  | Rated Input Current | 5A @ 115 VAC/3A @ 230 VAC |
|  |  | Maximum Rated Power | 200 Watts |
|  |  | Temperature (Values are subject to change) |  |
|  |  | Operating | 50( to 95(F/10( to 35(C |
|  |  | Non-operating | –4( to 140(F/–20( to 60(C |
|  |  | Humidity (non-condensing) (Values are subject to change) |  |
|  |  | Operating | 8% to 90% |
|  |  | Non-operating | 5% to 95% |
|  |  | Maximum Altitude (unpressurized) |  |
|  |  | Operating | 10,000 ft/3,048 m |
|  |  | Non-operating | 30,000 ft/9,144 m |
| Enhanced Keyboard |  | Dimensions (HxWxD) | 1.5 x 18 x 6.5 in/3.81 x 45.72 x 16.51 cm |  |
|  |  | Weight | 3.15 lbs/1.59 kg |  |
|  |  | Cable Length | 8 ft/2.4 m |  |
| 1.44-MB Diskette Drive |  | Diskette Size | 3.5 in |  |
|  |  | LED Indicators (front panel) | Green |  |
|  |  | Read/Write Capacity per Diskette (high/low) | 1.44 MB/720 KB |  |
|  |  | Drive Height | 1 in |  |
|  |  | Drive Rotation | 300 rpm |  |
|  |  | Transfer Rate (high/low) | 500/250 Kb/s |  |
|  |  | Bytes/Sector | 512 |  |
|  |  | Sectors/Track (high/low) | 18/9 |  |
|  |  | Tracks/Side (high/low) | 80/80 |  |
|  |  | Access Times |  |  |
|  |  | Track-to-Track (high/low) | 3/6 ms |  |
|  |  | Average (high/low) | 94/173 ms |  |
|  |  | Settling Time | 15 ms |  |
|  |  | Latency Average | 100 ms |  |
|  |  | Cylinders (high/low) | 80/80 |  |
|  |  | Read/Write Heads | 2 |  |

| Ultra3 (Ultra 160) SCSI Hard Drives (Ultra3 or Wide Ultra2 performance depending on controller) |  | 36.4 GB | Capacity | 18,209 MB | Seek Time (typical reads, including settling) |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Height | 1 in/25.4 mm | Single Track | 0.8 ms |
|  |  |  | Width | 3.5 in/88.9 mm | Average | 5 ms |
|  |  |  | Interface | Ultra3 (Ultra 160) SCSI or Wide Ultra2 SCSI | Full-Stroke | 13.5 ms |
|  |  |  | Transfer Rate |  | Rotational Speed | 10,000 rpm |
|  |  |  | Synchronous (Maximum) | 80 or 160 MB/s | Physical Configuration Bytes/Sector | 512 |
|  |  |  |  |  | Logical Blocks | 35,566,000 |
|  |  |  |  |  | Operating Temperature | 50( to 95(F/10( to 35(C |
|  |  | 18.2 GB | Capacity | 18,209 MB | Seek Time (typical reads, including settling) |
|  |  |  | Height | 1 in/25.4 mm | Single Track | 0.8 ms |
|  |  |  | Width | 3.5 in/88.9 mm | Average | 5 ms |
|  |  |  | Interface | Ultra3 (Ultra 160) SCSI or Wide Ultra2 SCSI | Full-Stroke | 13.5 ms |
|  |  |  | Transfer Rate |  | Rotational Speed | 10,000 rpm |
|  |  |  | Synchronous (Maximum) | 80 or 160 MB/s | Physical Configuration Bytes/Sector | 512 |
|  |  |  |  |  | Logical Blocks | 35,566,000 |
|  |  |  |  |  | Operating Temperature | 50( to 95(F/10( to 35(C |
|  |  | 9.1 GB | Capacity | 9,100 MB | Seek Time (typical reads, including settling) |
|  |  |  | Height | 1 in/25.4 mm | Single Track | 0.8 ms |
|  |  |  | Width | 3.5 in/88.9 mm | Average | 5 ms |
|  |  |  | Interface | Ultra3 (Ultra 160) SCSI or Wide Ultra2 SCSI | Full-Stroke | 13.5 ms |
|  |  |  | Transfer Rate |  | Rotational Speed | 10,000 rpm |
|  |  |  | Synchronous (Maximum) | 80 or 160 MB/s | Physical Configuration |  |
|  |  |  |  |  | Bytes/Sector | 512 |
|  |  |  |  |  | Logical Blocks | 17,773,500 |
|  |  |  |  |  | Operating Temperature | 50( to 95(F/10( to 35(C |
| Ultra ATA Hard Drives |  | 20.0 GB | Capacity | 20,000 MB | Seek Time (typical reads, including settling) |
|  |  |  | Height | 1 in/25.4 mm | Single Track | 1.7 ms |
|  |  |  | Width | 3.5 in/88.9 mm | Average | 8.5 ms |
|  |  |  | Interface | Ultra ATA/66 | Full-Stroke | 15.0 ms |
|  |  |  | Transfer Rate |  | Rotational Speed | 7200 rpm |
|  |  |  | Synchronous (Maximum) | 66.6 MB/s | Physical Configuration |  |
|  |  |  |  |  | Bytes/Sector | 512 |
|  |  |  |  |  | Logical Blocks | 39,102,336 |
|  |  |  |  |  | Operating Temperature | 41( to 131(F/5( to 55(C |
|  |  | 10.0 GB | Capacity | 10,000 MB | Seek Time (typical reads, including settling) |
|  |  |  | Height | 1 in/25.4 mm | Single Track | 1.7 ms |
|  |  |  | Width | 3.5 in/88.9 mm | Average | 8.5 ms |
|  |  |  | Interface | Ultra ATA/66 | Full-Stroke | 15.0 ms |
|  |  |  | Transfer Rate |  | Rotational Speed | 7200 rpm |
|  |  |  | Synchronous (Maximum) | 66.6 MB/s | Physical Configuration |  |
|  |  |  |  |  | Bytes/Sector | 512 |
|  |  |  |  |  | Logical Blocks | 19,541,088 |
|  |  |  |  |  | Operating Temperature | 41( to 131(F/5( to 55(C |
| 40X CD-ROM Drive |  | Disk Applicable Disk | CD-ROM (Mode 1 and 2), CD-DA, CD-R/W, Photo CD (Single and Multi-session), Mixed Mode (Audio and Data combined), CDI Ready, CD-XA Ready |
|  |  | Capacity | 540 MB (Mode 1, 12 cm) 650 MB (Mode 2, 12 cm) |
|  |  | Rotational Speed | 8,750 maximum |
|  |  | Diameter | 4.7 in, 3.15 in/12 cm, 8 cm |
|  |  | Center Hole | 0.6 in/15 mm diameter |
|  |  | Thickness | 0.05 in/1.2 mm |
|  |  | Track Pitch | 1.6 μm |
|  |  | Block Size |  |
|  |  | Mode 1 | 2,048 bytes |
|  |  | Mode 2 | 2,340, 2,336 bytes |
|  |  | CD-DA | 2,352 bytes |
|  |  | CD-XA | 2,328 bytes |
|  |  | Interface | IDE |
|  |  | Access Time (typical) |  |
|  |  | Random | < 100 ms |
|  |  | Full-Stroke | < 150 ms |
|  |  | Audio Output Level |  |
|  |  | Line-Out | 0.7 VRMS |
|  |  | Data Transfer Rate |  |
|  |  | Sustained | 150 KB/s (1X, using audio disc) |
|  |  | Variable | 2,550 to 6,000 KB/s (17X to 40X with 650 MB disc) |
|  |  | Cache Buffer | 128 KB minimum |
|  |  | Start-up Time (typical) | < 7 s |
|  |  | Stop Time (typical) | < 4 s |
|  |  | Operating Conditions |  |
|  |  | Temperature | 41° to 113°F/5° to 45°C |
|  |  | Humidity | 10% to 80% |
|  |  | Dimensions (HxWxD, maximum) | 1.7 x 5.9 x 8.19 in/4.29 x 15 x 20.8 cm |
|  |  | Weight | 2.65 lbs/1.2 kg |
| Compaq Premier(Sound featuring AC’97 Audio |  | Type | Embedded AC’97 2.1 Codec |
|  |  | Sound Quality | 16-Bit Stereo Full-Duplex (CD Quality) |
|  |  | Sampling | Variable 7 kHz to 48 kHz |
|  |  | Audio Compression/ Decompression | ESPCM and ADPCM compression |
|  |  | Full Scale Input Voltage (RMS) |  |
|  |  | Microphone Input | 100 mVolts |
|  |  | Line Input | 2.2 Volts |
|  |  | Full Scale Output Voltage (RMS) |  |
|  |  | Line Output | 1.4 Volts |
|  |  | Impedance (nominal) |  |
|  |  | Line Output | 800 ohms (typical) |
|  |  | Line Input | 10 K ohms (typical) |
|  |  | Playback (PC-D-A) |  |
|  |  | Dynamic Range | –91 dB (typical) |
|  |  | Total Harmonic Distortion + Noise | –69 dB (typical) |
|  |  | Frequency Response (-3 dB) | 20 Hz to 20 kHz |
|  |  | Line Output Crosstalk (10 kHz) | –74 dB |
|  |  | Headphone Maximum Output (1 kHz) | 60 mWrms into 32 ohms (THD+N < 1.0%) |
|  |  | Internal Power Amplifier Rating | Nominal: 1.5 Watts RMS @ 8 ohms Maximum: 5 Watts RMS @ 8 ohms |
|  |  | Speaker |  |
|  |  | Frequency Response | 200 Hz to 15 kHz |
|  |  | Equalizer | 5 stages of fixed equalization |
|  |  | Design | High-performance, infinite baffle loudspeaker |
|  |  | Connectors | Line-in, line-out, microphone in, headphone out |
|  |  | Operating System Driver Support | Windows NT 4.0, Windows 95, Windows 98, Windows 2000 |
| Intel PRO/100+ Management Adapter |  | Network Interface | 10Base-T or 100Base-TX |
|  |  | Expansion Bus Architecture | PCI 2.2 |
|  |  | Network Transfer Rate |  |
|  |  | 10Base-T (Half-Duplex) | 10 Mb/s |
|  |  | 10Base-T (Full-Duplex) | 20 Mb/s |
|  |  | 100Base-TX (Half-Duplex) | 100 Mb/s |
|  |  | 100Base-TX (Full-Duplex) | 200 Mb/s |
|  |  | Connectors | RJ-45 |
|  |  | Standards Compliance |  |
|  |  | 10-MB/s Ethernet | IEEE 802.3 |
|  |  | 100-Mb/s Ethernet | IEEE 802.3( |
|  |  | I/O Address | Auto-configured |
|  |  | Remote Wakeup | Yes |
|  |  | Temperature |  |
|  |  | Operating | 0( to 55(F/10( to 35(C |
|  |  | Humidity (non-condensing) |  |
|  |  | Operating | 85% at 131(F/55(C |
|  |  | Altitude |  |
|  |  | Operating | 10,000 ft/3,048 m |
|  |  | Communication Processor | Intel 82559 |
|  |  | OS Driver Support |  |
|  |  | Windows NT 4.0 | NDIS 3.0, 4.0 Compliant |
|  |  | Windows 95, 98, 2000 | NDIS 3.0, 4.0, 5.0 Compliant |
|  |  | Novell NetWare Server v. 3.x, 4.x and 5.0 | ODI Compliant |
|  |  | SunSoft Solaris | Not supported |
|  |  | SCO UnixWare, OpenDesktop, OpenServer | Supported |

| Matrox G200 Quad Multi-Monitor Series (MMS) Graphics Controller |  | Dimensions (HxW) | 4.5x8 in/11.43x20.32 cm |
| --- | --- | --- | --- |
|  |  | Refresh Rate (per display) |  |
|  |  | Aspect Ratio | Resolution | Vertical | Horizontal |
|  |  | 4:3/5:4 | 640 x 480 | 60-200 Hz | 31-102 kHz |
|  |  |  | 800 x 600 | 60-200 Hz | 38-114 kHz |
|  |  |  | 1024 x 768 | 60-140 Hz | 48-113 kHz |
|  |  |  | 1152 x 864 | 60-120 Hz | 54-110 kHz |
|  |  |  | 1280 x 1024 | 60-100 Hz | 64-107 kHz |
|  |  |  | 1600 x 1200 | 60-90 Hz | 75-113 kHz |
|  |  |  | 1800 x 1440 | 60-70 Hz | 89-104 kHz |
|  |  | 16:9/16:10 | 856 x 480 | 60-200 Hz | 30-108 kHz |
|  |  |  | 1280 x 720 | 60-100 Hz | 44-76 kHz |
|  |  |  | 1600 x 1024 | 60-100 Hz | 64-108 kHz |
|  |  |  | 1920 x 1080 | 60-80 Hz | 70-94 kHz |
|  |  |  | 1920 x 1200 | 60-76 Hz | 75-95 kHz |
|  |  | With DVI digital flat panel displays, the maximum display resolution is 1280 x 1024 |
|  |  | Maximum refresh rates may not be attainable at the highest display resolutions with 24 or 32-bit color palettes |
|  |  | Interface | PCI |
|  |  | Standard Memory | 32 MB SGRAM (8 MB per port) |
|  |  | DAC Speed | 250 MHz |
|  |  | Data Path | 128-bit Internal/64-bit External |
|  |  | Color Space Conversion | Yes |
|  |  | Scaling | Yes |
|  |  | Quick Draw Support | Yes |
|  |  | DCI & DirectX Video Playback | Yes |
|  |  | Direct3D Support | Yes |
|  |  | Engine Acceleration | 3 ROP bitBLT, Line Draw, Text, Color Expansion, Basic Video Color Conversion and Scaling, Triangle Setup Engine |
|  |  | Output | Two output ports, which require 2 adapter cables to connect analog or digital output displays |
|  |  | Analog Display Support | 2 RGB cables support two DB-15 analog displays per cable |
|  |  | DVI (Digital Visual Interface) Display Support | DVI cable option kit provides two DVI cables for connecting two DVI compliant displays per cable |
|  |  | Display options supported | Four analog displays via two RGB cables Four DVI displays via two DVI cables Two analog displays via one RGB cable and two DVI displays via one DVI cable |
|  |  | Other | PCI bus mastering, texture mapping support, flat and Gouraud shading, Anisotropic Filter, perspective texture, specular highlighting, dithering, full scene anti-aliasing, Vertex fog |
|  |  | OS Support | Windows NT 4.0 and Windows 2000 |

| Compaq NVIDIA TNT2 Pro™ Graphics Controller |  | Form Factor | 1/2 size ATX |
| --- | --- | --- | --- |
|  |  | Bus Type | AGP |
|  |  | Memory Support | 16MB SGRAM |
|  |  | RAMDAC | 300MHz |
|  |  | Data Path | 128-bit |
|  |  | Process | 0.25u |
|  |  | Internal Clock | 142 MHz |
|  |  | Memory Clock | 166 MHz |
|  |  | Pipelines | 2 (bilinear) |
|  |  | Fill Rate | 333 M pix/sec |
|  |  | Triangle Rate | 8 M Tri/sec |
|  |  | Video Overlay Filter | 2x2 |
|  |  | Color Space Conversion | Yes |
|  |  | Scaling | Yes |
|  |  | Feature Connector | VIP connector |
|  |  | Quick Draw Support | Yes |
|  |  | DCI & DirectX Video Playback | Yes |
|  |  | MS Direct X Support | Yes |
|  |  | 3D Support | Yes |
|  |  | Engine Acceleration | Basic Video Color Conversion and Scaling |
|  |  |  | Triangle Setup Engine |
|  |  | OS Support | Windows 95, 98, Windows 2000, Windows NT 4.0 |
|  |  | Other |  |
|  |  |  | Optimized for Direct3D acceleration with support for DirectX 5.0 and 6.0 |
|  |  |  | 16 MB Frame Buffer - 166 MHz SGRAM |
|  |  |  | 128-bit TwiN-Texel (TNT) architecture |
|  |  |  | 2 texture mapped, lit pixels per clock |
|  |  |  | Single pass multi-texture rendering |
|  |  |  | 32-bit rendering with destination alpha |
|  |  |  | 24-bit Z-buffer, 8-bit stencil buffer |
|  |  |  | Anisotropic filtering (better than Tri-Linear MIP-mapping) |
|  |  |  | 100% hardware triangle setup engine |
|  |  |  | High performance 128-bit 2D/GUI/DirectDraw Acceleration. Transparent BLT, stretch BLT, points, lines, polylines, polygons, fills, patterns, arbitrary clipping and fast text rendering. Pipe-line optimized for multiple color depths including 8, 16, and 24 bits per pixel |
|  |  |  | Video acceleration for DirectShow™, MPEG-1, MPEG-2 and Indeo ® |
|  |  |  | Fast 32-bit VGA/SVGA |
|  |  |  | 128-bit frame buffer interface - 2.6 Gbytes/sec bandwidth |
|  |  |  | Triple 8-bit 250MHz Palette DAC |
|  |  |  | Bi-directional Media Port and CCIR-656 Video Capture Port (for AIB only) |
|  |  |  | AGP 4X/2X system bus with full sideband support |
| Compaq NVIDIA TNT2 Pro Graphics Controller (continued) |  | Resolutions Supported |  |
|  |  | 1800 x 1440 |  |
|  |  | Windows Resolution & Colors | 256, 65K, 16.7M |
|  |  | Real-Time 3D Gouraud Shading | 65K |
|  |  | Refresh Rates | V(60 to 70 Hz) H(89 to 104kHz) |
|  |  | 1920 x 1200 |  |
|  |  | Windows Resolution & Colors | 256, 65K, 16.7M |
|  |  | Real-Time 3D Gouraud Shading | 256, 65K |
|  |  | Refresh Rates | V(60 to 76 Hz) H(75 to 95kHz) |
|  |  | 1920 x 1080 |  |
|  |  | Windows Resolution & Colors | 256, 65K, 16.7M |
|  |  | Real-Time 3D Gouraud Shading | 256 |
|  |  | Refresh Rates | V(60 to 80 Hz) H(70 to94kHz) |
|  |  | 1600 x 1200 |  |
|  |  | Windows Resolution & Colors | 256, 65K, 16.7M |
|  |  | Real-Time 3D Gouraud Shading | 256 |
|  |  | Refresh Rates | V(60 to 90 Hz) H(75 to 113kHz) |
|  |  | 1280 x 1024 |  |
|  |  | Windows Resolution & Colors | 256, 65K, 16.7M |
|  |  | Real-Time 3D Gouraud Shading | 256, 65K |
|  |  | Refresh Rates | V(60 to 100 Hz) H(64 to 107kHz) |
|  |  | 1152 x 864 |  |
|  |  | Windows Resolution & Colors | 256, 65K, 16.7M |
|  |  | Real-Time 3D Gouraud Shading | 256, 65K |
|  |  | Refresh Rates | V(60 to 120 Hz) H(54 to 110kHz) |
|  |  | 1024 x 768 |  |
|  |  | Windows Resolution & Colors | 256, 65K, 16.7M |
|  |  | Real-Time 3D Gouraud Shading | 256, 65K, 16.7M |
|  |  | Refresh Rates | V(60 to 140 Hz) H(48 to 113kHz) |
|  |  | 800 x 600 |  |
|  |  | Windows Resolution & Colors | 256, 65K, 16.7M |
|  |  | Real-Time 3D Gouraud Shading | 256, 65K, 16.7M |
|  |  | Refresh Rates | V(60 to 200Hz) H(38 to 114kHz) |
|  |  | 640 x 480 |  |
|  |  | Windows Resolution & Colors | 256, 65K, 16.7M |
|  |  | Real-Time 3D Gouraud Shading | 256, 65K, 16.7M |
|  |  | Refresh Rates | V(60 to 200 Hz) H(31 to102kHz) |
| Matrox Millennium G400 Graphics Controller |  | Single Display Dimensions (HxW) | 3.25 x 6.75 in/8.26 x 17.15 cm |
|  |  | Dual Display Dimensions (HxW) | 3.25 x 6.75 in/8.26 x 17.15 cm |
|  |  | Resolution (DualHead second analog output supports maximum resolution of 1280x1024x16.7 M colors at up to 75 Hz. DVI daughter board enables output at 1280x16.7M colors at 85 Hz) | 256 Colors | 65K Colors | 16.7M Colors |
|  |  | 640 x 480 | 85 Hz | 85 Hz | 85 Hz |
|  |  | 800 x 600 | 85 Hz | 85 Hz | 85 Hz |
|  |  | 1024 x 768 | 85 Hz | 85 Hz | 85 Hz |
|  |  | 1152 x 864 | 85 Hz | 85 Hz | 85 Hz |
|  |  | 1280 x 1024 | 85 Hz | 85 Hz | 85 Hz |
|  |  | 1600 x 1200 | 85 Hz | 85 Hz | 85 Hz |
|  |  | 1800 x 1440 | 85 Hz | 85 Hz | 85 Hz |
|  |  | 1800 x 1440 | 85 Hz | 85 Hz | 85 Hz |
|  |  | 1920 x 1080 | 85 Hz | 85 Hz | 85 Hz |
|  |  | 1920 x 1440 | 75 Hz | 75 Hz | 75 Hz |
|  |  | 2048 x 1536 | 65 Hz | 65 Hz | 65 Hz |
|  |  | 2D Controller | Matrox G400 |
|  |  | VGA Controller | Integrated |
|  |  | Bus Type/Speed | AGP 4X |
|  |  | RAMDAC | Integrated |
|  |  | DAC Speed | 300 MHz |
|  |  | Memory Type | SGRAM |
|  |  | Memory Amount | 16 MB |
|  |  | Maximum Memory Speed | 120 MHz |
|  |  | Data Path | 128-bit external/256-bit internal |
|  |  | Controller Clock Speed | 120 MHz |
|  |  | Maximum Pixel Clock | 360 MHz |
|  |  | Video Interface |  |
|  |  | Single Display | Analog (digital available with optional Millennium G400 DVI Daughter Board) |
|  |  | Dual Display | Analog, 2 ports |
|  |  | Engine Acceleration | 3 ROP bitBLT, Line Draw, Text, Color Expansion, Basic Video Color Conversion and Scaling, Triangle Setup Engine |
|  |  | Other | Color Space Conversion, Scaling, Quick Draw support, DCI and DirectX Video Playback, MS DirectDraw support, 3D support, PCI bus mastering, texture mapping support, flat and gouraud shading, direct 3D support, anisotropic filter, perspective texture, specular highlighting, wireframe, dithering, full scene anti-aliasing, OpenGL support, vertex fog, dual texture mapping, environment bump mapping AGP 2X/4X with sideband addressing |
|  |  | Operating Systems | Windows NT 4.0, Windows 95, Windows 98, Windows 2000 |

| ELSA Synergy II Graphics Controller |  | Dimensions (HxW) | 3.25 x 6.25 in/8.3 x 15.9 cm |
| --- | --- | --- | --- |
|  |  | Resolution | Maximum Colors Supported | Maximum Refresh Rate | Memory Dedicated to Texture Support |
|  |  | 640 x 480 800 x 600 1024 x 768 1152 x 864 1280 x 1024 1600 x 1000 1600 x 1000 1600 x 1200 1600 x 1200 1600 x 1280 1600 x 1280 1920 x 1080 1920 x 1080 1920 x 1200 1920 x 1200 | 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M 65K 16.7M 65K 16.7M 65K 16.7M 65K 16.7M 65K | 120 Hz 120 Hz 120 Hz 120 Hz 120 Hz 75 Hz 85 Hz 75 Hz 85 Hz 75 Hz 85 Hz 75 Hz 85 Hz 75 Hz 75 Hz | 29.1 MB 27.1 MB 23.5 MB 21.1 MB 17.9 MB 14 MB 14 MB 10.2 MB 10.2 MB 8.7 MB 8.7 MB 8.4 MB 8.4 MB 5.7 MB 5.7 MB |
|  |  | 3D/2D Controller VGA Controller Bus Type | Nvidia TNT 2 Integrated AGP 2X/4X |
|  |  | RAMDAC | Integrated 300 MHz |
|  |  | Memory Type | SDRAM |
|  |  | Memory Amount | 32 MB (Maximum) |
|  |  | Memory Speed | 143 MHz |
|  |  | Controller Clock Speed | 125 MHz |
|  |  | Color Planes | 24 bits double buffered |
|  |  | Stencil Planes | 8 bit |
|  |  | Alpha Planes | 0 |
|  |  | Z-buffer | 24 bit |
|  |  | Total bits/pixel | 96 |
|  |  | Maximum Vertical Refresh Rate | 120 Hz |
|  |  | Maximum Pixel Clock | 300 MHz |
|  |  | Multi-display Support | No |
|  |  | Operating Systems | Windows NT 4.0, Windows 95, Windows 98 |

Note: All drivers and enhanced software, including POWERdraft, ELSAview, and MAXtreme, can be found on the Compaq web site at: www.compaq.com/support/files/workstations/us/index.html.

| ELSA GLoria II Graphics Controller |  | Dimensions (H x W) | 3.25 x 6.25 in/8.3 x 15.9 cm |
| --- | --- | --- | --- |
|  |  | Resolution | Maximum Colors Supported | Maximum Refresh Rate | Memory Dedicated to Texture Support |
|  |  | 640 x 480 800 x 600 1024 x 768 1152 x 864 1280 x 800 1280 x 960 1280 x 1024 1600 x 1000 1600 x 1000 1600 x 1200 1600 x 1280 1600 x 1280 1920 x 1080 1920 x 1080 1920 x 1200 1920 x 1200 2048 x 1536 | 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M | 120 Hz 120 Hz 120 Hz 100 Hz 100 Hz 100 Hz 100 Hz 100 Hz* 85 Hz 85 Hz 85 Hz* 75 Hz 85 Hz* 75 Hz 85 Hz* 75 Hz 75 Hz* | 60 MB 58 MB 54 MB 52 MB 52 MB 49 MB 48 MB 45 MB 45 MB 41 MB 40 MB 40 MB 39 MB 39 MB 37 MB 37 MB 27 MB |
|  |  |  | *Refresh rate may function but may not officially be supported by Compaq monitors. |
|  |  | 3D/ Controller VGA Controller Bus Type | NVIDIA Quadro Integrated AGP 2X/4X |
|  |  | RAMDAC | Integrated 350 MHz |
|  |  | Memory Type | SDRAM |
|  |  | Memory Amount | 64 MB (unified) |
|  |  | Memory Speed | 166 MHz |
|  |  | Controller Clock Speed | 135 MHz |
|  |  | Color Planes | 24-bit double buffered |
|  |  | Overlay Planes | 8-bit double buffered |
|  |  | Stencil Planes | 8-bit |
|  |  | Alpha Planes | 8-bit double buffered |
|  |  | Z-buffer | 24-bit |
|  |  | Total bits/pixel | 112 |
|  |  | Maximum Vertical Refresh Rate | 132 Hz |
|  |  | Maximum Pixel Clock | 350 MHz |
|  |  | Multi-display support | No |
|  |  | Stereo support | Available Spring 2000 |
|  |  | Operating Systems | Windows NT 4.0 |

| 3Dlabs Oxygen GVX1 Graphics Controller (Not all settings are supported on all monitors.) |  | Dimensions (HxW) | 4.25 x 9.283 in/10.795 x 23.58 cm |
| --- | --- | --- | --- |
|  |  | Resolution | Maximum Colors Supported | Maximum Refresh Rate |
|  |  | 640 x 480 1024 x 768 1152 x 864 1280 x 1024 1600 x 1200 1920 x 1080 1920 x 1200 | 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M 16.7M | 100 Hz 100 Hz 100 Hz 100 Hz 85 Hz 85 Hz 76 Hz |
|  |  | 3D Controller Geometry Bus Type | GLINT R3 GLINT Gamma G1 AGP |
|  |  | RAMDAC | Integrated |
|  |  | Memory Type | SGRAM |
|  |  | Memory Amount | 32 MB (maximum) |
|  |  | Memory Speed | 125 MHz |
|  |  | Controller Clock Speed | 125 MHz |
|  |  | Color Planes | 24 bit double buffered |
|  |  | Overlay Planes | 8 bit shared with alpha |
|  |  | Stencil Planes | 8 bit with 24-bit Z-buffer |
|  |  | Alpha Planes | 8 bit shared with overlay |
|  |  | Z-buffer | 24 bit (32 bit with no stencil) |
|  |  | Total bits/pixel | 96 |
|  |  | Maximum Vertical Refresh Rate | 120 Hz |
|  |  | Maximum Pixel Clock | 300 MHz |
|  |  | Dual Display Support | Yes (with additional optional GVX1 PCI card) |
|  |  | Operating Systems | Windows NT 4.0 |
|  |  | Stereographics Support | Yes |
|  |  | Resolution/Refresh Rates Supported for Stereographics Functionality |  |
|  |  | Resolution | Maximum Colors Supported | Maximum Refresh Rate |
|  |  | 1152 x 864 1280 x 800 1280 x 960 1280 x 1024 | 16.7M 16.7M 16.7M 16.7M | 132 Hz 118 Hz 118 Hz 118 Hz |

# Text boxes

Models

Compaq Deskpro Workstation AP250

Available in multiple configurations.  Not all configurations available in all countries.  Check with your Authorized Compaq Reseller or Compaq.

At A Glance

One Intel Pentium®  III processor 600EB, 733 or 866 MHz with 
133-MHz Front Side Bus

Intel 820 chipset with 
AGP4X support

256-KB Level 2 cache integrated on processor

128 or 256 MB of ECC RDRAM, expandable up to 512 MB (1 GB when 288-Mb technology  becomes available)

High-performance 9.1-GB  or 18.2-GB (10,000 rpm) Ultra3 (Ultra 160) SCSI or 20-GB 
(7200 rpm) Ultra ATA/66 SMART 
hard drive

Choice of graphics controllers: NVIDIA TNT2 Pro, Matrox Millennium G400, ELSA GLoria II, ELSA  Synergy II, 3Dlabs Oxygen GVX1, or Matrox G200 Quad MMS

Convertible minitower form factor with external drives that rotate 90°, easily converting from minitower to desktop

Intel PRO/100+ Management Adapter NIC (10/100 Mb/s Autosensing Ethernet Controller) PCI with Wake-on-LAN and 
Alert-on-LAN, capable of operating in either 10Base-T or 100 Base-TX environments

32-bit, PCI-based system

Seven total slots (four PCI, one shared PCI/ISA, one ISA, 
one AGP)

Five bays (three user-accessible, two internal)

40X CD-ROM

Embedded audio with integrated Premier(SoundTM  speaker

Windows NT Workstation 4.0 or Windows 2000 Professional (depending on model) and Compaq support software 
pre-installed

Intelligent Manageability features

- Protected by Compaq services, including a three-year limited warranty — Certain restrictions and exclusions apply. Consult the Compaq Customer Support Center for details. Three year onsite and labor not available in all countries.

Compaq Color Monitor (optional)

1.44-MB Diskette Drive

40X Max CD-ROM Drive (IDE)

User-accessible Drive Bay

Compaq Three-button Mouse

Compaq Keyboard

Power Switch with LEDs

NIC Controller in PCI Slot

SCSI Controller in PCI Slot (on select models)

Speaker

Processor

200-Watt Power Supply

Memory Module Sockets

Drive Lock