PKTDLL v1.1

PKTDLL provides a Packet Driver interface over Digital Equipment Corp.'s
Datalink (DLL) specification drivers.  This is a small TSR shim which
translates application Packet Driver calls into appropriate DLL calls.
PKTDLL should work over any of the current V4.1 DLL and earlier drivers
(DLLDEPCA, DLLNDIS, etc.), making it a simple matter to add Packet Driver
applications to an existing PATHWORKS network environment.  Simply add a
line with "PKTDLL" into your AUTOEXEC.BAT after the commands to start the
network.  If you feel really adventurous you could even "LOADHIGH PKTDLL"
(it works fine!).

PKTDLL was renamed from DLLPKT to be consistent with the naming conventions
used within Digital Equipment Corporation and the left to right reading
habits of the western world.  If you feel stubborn about this issue, DOS
does have a file renaming command.

I have not included support for any advanced functionality such as
multicast and promiscuous mode.  If there are significant grumblings, I
will re-examine these issues, however, I really don't see the need.  This
extra functionality is better served by existing utilities which deal
directly with the DLL.

There is an assumption that the DECnet flavour of PATHWORKS is being used.
Having two different TCP/IP stacks simultaneously on a single machine would
be somewhat strange (perhaps it would be ok with multiple network cards).
Also, PKTDLL is currently setup as a Class 1 Packet Driver (ethernet).  I
will soon be examining the changes required to support Token Ring.  I have
also made this a so called high performance Packer Driver, but there has
been a minimum of testing with the high performance functions.  This may
sound somewhat tentative, however, I have been using the driver regularly
for quite some time and have found no problems.

If you have the desire to modify this code or find items needing repair,
please send me your requests and/or updates.  I am closer to DEC's
engineering group and should be able to ensure that PKTDLL functions
according to the DLL specification, hopefully keeping so called quality at
a high level.  Please also forward any other comments to me.  I am quite
interested in how people may be using this driver.

The following packages have been successfully tested with PKTDLL:
WATTCP                          NCSA Telnet
KA9Q                            CUTCP
Kermit                          QVTNET
Trumpet - News Reader           PDIPX from Intel
Trumpet - TCPDRV                IPX from BYU
PKTMUX                          WINPKT


Usage:                  PKTDLL [packet_int] [proto_type...] [/n] [/u]

packet_int      -       This is the Packet Driver interrupt to use.  The
			default interrupt is 61 HEX.  The number will be
			interpreted as hexadecimal whether or not it is
			prefixed by "0x".  This same rule applies to the
			protocol type following.

			range: 60 - 7F

proto_type      -       This is a list of protocol types to hold open for
			Windows access.  The DLL must have any protocols
			which it will use in Windows opened prior to
			entering Windows.  The protocols in this list will 
			be opened and held in limbo until accessed by an
			application.  There is no such restriction on Packet
			Driver applications outside of Windows.

			The default is to open protocols 0800, 0806, and
			8035 (IP, ARP, and RARP).  This list may replaced
			by a list of your own choosing.  Be aware that the
			DLL only supports 8 portals, several of which are
			often used by PATHWORKS.  MOP and LoopBack are
			temporarily disabled when PKTDLL is loaded but are
			restored on exiting PKTDLL.

			range: 05EF - FFFE

/n              -       "/n" will select 802.3 framing for Novell's IPX.
			Most public domain IPX stacks use Novell's 8137
			DIX protocol type.  This will convert these packets
			to 802.3 on the wire.  This functionality will not
			work with the new PATHWORKS V5.x DLL drivers being
			developed - ie. only DIX will be supported (the API
			changed and I am feeling very lazy).

/u              -       "/u" will unload the driver releasing both its
			memory and it reserved protocols, provided there
			are none in use.  If an alternate interrupt has
			been chosen, it must be specified when unloading
			the driver.


Examples:               PKTDLL

			Loads the Packet Driver at interrupt 61 with protocols
			IP, ARP and RARP active for Windows.

			PKTDLL 60 7301 7302 /n

			Loads the Packet Driver at Interrupt 60 with protocols
			7301 and 7302 (just made them up!) active for Windows.
			If you want to reserve some other protocol, you must
			specify the Packet Driver interrupt (sorry).  Also,
			protocol 8137 will be converted to 802.3.

			PKTDLL 60 /u

			Unloads the Packer Driver loaded at interrupt 60.


Have Fun,

Brian Angus

angus@trcoa.enet.dec.com
(416) 597-3268