NetWare Workstation for OS/2 v2.01
                            Readme file


Remote Workstations Not Supported
-----------------------------

The files needed to install and use remote workstations are not included in 
this release. The RIPL files will be available at a later date.


Frame Type Default Is Different
--------------------------

The default frame type for Ethernet ODI drivers (such as NE2000.SYS) has 
changed. In NetWare v3.x and NetWare v2.x, Ethernet drivers defaulted to 
Ethernet_802.3. In NetWare v4.0, they default to Ethernet_802.2. 

NetWare v4.0 server drivers for Ethernet also default to Ethernet_802.2. 
Servers and workstations use the same frame type to communicate with each 
other. 

Routers on the network also have to support the frame type or your 
workstation often will not be able to get a connection. Some routers 
currently in use on your network may not support the new Ethernet_802.2 
default. 

Your workstation may not be able to connect to a network expecting 
Ethernet_802.3 if you use the Ethernet_802.2 default. 

To eliminate a potential conflict, you can define both frame types 
(Ethernet_802.2 and Ethernet_802.3) on your network. For the workstation, 
define frame types in the NET.CFG file.  Include a line similar to the 
following, replacing NE2000 with the name of your ODI driver:

     link driver ne2000
     frame ethernet_802.2
     frame ethernet_802.3

The first frame defined is the only one used for the initial Get Nearest 
Server request. Therefore, if you have some servers that are using only one 
frame type, such as Ethernet_802.3, put that frame type first. That way 
your workstation will be able to make a default connection to those servers.

See Chapter 5, "Network Boards and Drivers" of NetWare Workstation for OS/2
for more information about frame type. 


Logging In From Global DOS Not Supported
----------------------------------

Do not log in from a global DOS session. Instead, log in from an OS/2 
session and then switch to the DOS session. 

Except for this login difference, you can still set up drive mappings for 
global sessions as instructed in Chapter 3, "Network Access From Virtual 
DOS and Windows" of NetWare Workstation for OS/2. 


Editing Login Scripts for DOS Sessions
--------------------------------

If a user logs in from a private DOS session running NETX.EXE, a NetWare
v3.11 user login script will execute if it exists. This login script is 
called LOGIN and is located in the SYS:MAIL\userID directory. You can edit
it with a text editor or a bindery utility from previous versions of NetWare
such as SYSCON.

If the server is a new NetWare v4.0 installation rather than an upgrade, 
login scripts and the \MAIL\userID directory will not exist. Login scripts 
in NetWare 4.0 are properties of the user object.

You can create the login script on a local drive and use the /S option when
you login. For example, create the LOGIN.DOS login script on the C:\ drive
and type the following to log in:

     LOGIN /S C:\LOGIN.DOS


Running NetWare v4.0 Utilities in DOS_STARTUP_DRIVE Sessions
------------------------------------------------------

In a private DOS session booted from a real DOS kernel (i.e., a session 
with DOS_STARTUP_DRIVE set) running NetWare v4.0 DOS Requester, you may 
receive errors running some of the utilities. 

Solve the problem by being logged in from an OS/2 session whenever you use
a utility from the DOS_STARTUP_DRIVE session. You must be logged in to the
same server from the OS/2 session as you are logged in to from the 
DOS_STARTUP_DRIVE session. 

For example, suppose you logged into server SALES from the 
DOS_STARTUP_DRIVE session. For some utilities to function, you would also 
need to log in to server SALES from an OS/2 session. As long as your OS/2 
session is logged in, your utilities will function properly. 

This condition particularly applies to the PCONSOLE, NETUSER, FILER, NDIR,
and NPRINT utilities.


Request Retries Default Incorrect
---------------------------
The Workstation for OS/2 manual and online help incorrectly document the
default for the "NetWare Requester request retries" NET.CFG setting. The 
correct default is 10, not 20. This lower default helps minimize transmission
errors with slower ODI drivers.