## Slide 1: Computing Hardware Architecture & Performance
Bob Kuehne, SGI
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: Course Overview
Why is your application drawing so slowly?
  Could actually be the graphics
  Could be the data traversal
  Could be something entirely different
Notes: <number>
<footer>
<header>
<date/time>
Premise
- app not drawing as fast as expected
Why?
- many reasons are possible
Goal
- cover some of those reasons, from a hardware perspective

## Slide 3: Tour Guide
Platform architecture & components
  CPU
  Memory
  Graphics
Graphics performance
  Measurements: triangle rate, fill rate, misc.
  Reproduce & maximize
Notes: <number>
<footer>
<header>
<date/time>
- talk about architectures
- cpu/memory systems
- graphics systems and a taxonomy for classification
- graphics hardware performance
- what it means
- how to duplicate
** please read the course notes for much much more detail in any o fhtese areas **

## Slide 4: Bottlenecks & Balance
Bottlenecks
  Find them
  Eliminate them (sort of - move them around)
Balance
  Understand hardware architecture
  Fully utilize hardware
Notes: <number>
<footer>
<header>
<date/time>
Premise
- focus further: removing bottlencecks, balancing system util
Bottlenecks
- definition: bottleneck: portion of app which limits overall perf
(and in this case, the graphics rendering perf)
Bottleneck Ident:
- bottlencks are slippery and elusive creatures
- one app, one dataset, a particular bottlenck
- diff dataset, diff bottleneck
- diff platform, diff problems
Bottleneck Squash:
- once one is squashed, likely will move to another place.
- Rinse, repeat.
Which brings us to balance.
- again, the goal is to eliminate bottlenecks through balance
- to do that, must

## Slide 5: Yin & Yang
  “Yin and yang are the two primal cosmic principles of the universe”
  “The best state for everything in the universe is a state of harmony represented by a balance of yin and yang.”
    Skeptics Dictionary -- http://skepdic.com/yinyang.html
Notes: <number>
<footer>
<header>
<date/time>
Tangent!
- icon to draw attention balance
- not an exact philosophical match, but it looks nice
- trying to make point, again and again, that balanced system utilization is key. Wha twe hope to provide is awareness of a number of ideas and issues which can help you to attain a harmonious balance of system utilization
- a key to balancing system utilization is to first understand the application and the system on which it runs
- so, we begin with hardware

## Slide 6: Write Once Run Everywhere?
My application ran fast on that platform! Why is this one so slow?
  Different platforms require different tuning
  Different platforms implement hardware differently
    Macro: Architecture & features
    Micro: Storage capacities, buffers, & caches
    Effect: Bandwidth & latency
Notes: <number>
<footer>
<header>
<date/time>
- sw dev exp” write once, run somewhere else, slower.
- digging reveals an implementatino decision defect
- problem rooted in the fact that different systems implement
different hardware (cpu, gfx, memory, disk, net) in different ways.
- why? Because each vendor has a better idea. System level stuff, as well as gfx.
- talk about differences
macro: systems differ within basic architectures:
micro: data flow things
affects: bandwidth and latency to do real work
example:
- gfx w/texture, gfx w/o tex + accum
- gfx on agp, gfx on dedicated link to memory, etc.

## Slide 7: Latency & Bandwidth
Definitions
  Latency: time required to communicate a unit of data
  Bandwidth: data transferred per unit time
Notes: <number>
<footer>
<header>
<date/time>
Before talking more about hardware, it’s important to understand two aspects of data transfer which affect all apps, these are latency and bandwidth.
- def: latency: time required to do something.
- data from disk, bit from memory, state on gfx
- min time to complete a communication with something
- def bw:
- amount of data can be transferred in a specific time
- disk 80MB/s, network 10Mb/s, mem 3Gb/sec
- ex:
- each box represents unit of time
latency is relevant many places. We’ll talk more about it throughout the course. For now, back to architectures.

## Slide 8: Latency & Bandwidth
Example:
  Latency bottleneck
  Bandwidth bottleneck
S
t
S
t
S
t
S
t
S
t
S
t
t
t
t
S
t
t
t
: unit of time
s: texture setup time
t: texture download time
Notes: <number>
<footer>
<header>
<date/time>
Before talking more about hardware, it’s important to understand two aspects of data transfer which affect all apps, these are latency and bandwidth.
- def: latency: time required to do something.
- data from disk, bit from memory, state on gfx
- min time to complete a communication with something
- def bw:
- amount of data can be transferred in a specific time
- disk 80MB/s, network 10Mb/s, mem 3Gb/sec
- ex:
- each box represents unit of time
latency is relevant many places. We’ll talk more about it throughout the course. For now, back to architectures.

## Slide 9: Platform: Software View
graphics
i/o
misc
memory
CPU
net
Notes: <number>
<footer>
<header>
<date/time>
- I present an absctract system to discuss how data moves in a computing platform.
- a gfx app does many things, wave hands around for a bit.
- disk/net io
- stuff data in memory, compute, tesselate, etc
- shove data to graphics, get data from graphics
- you know what your app does, so why are you telling me this, and how do I write better code? Wait for it … wait for it …
- this cloud, manages that. What is the cloud, and how does it work?
- will describe shortly
- think about how these paths are used to transfer data, and which
are used by your app.
-shortened or elim data path app is faster.
-Less hardware in way
-point: in certain modes of op, app doing particular things, to particular parts of the system. Understanding what parts are in use is key to maximizing performance.

## Slide 10: Platform: PCI, AGP
CPU
Memory
Disk
Net
Graphics
I/O
PCI
glue
CPU
glue
Memory
Disk
Net
Graphics
I/O
PCI
AGP
Notes: <number>
<footer>
<header>
<date/time>
- PCI: cpu, memory, and PCI are controlled by the glue, while all
devices live on a shared bus (PCI).
- gfx on bus, local mem for fb, tex, etc.
- all devices compete for scarce resource, bandwidth,
-AGP: cpu, memory, pci, and agp are directly controlled byt the glue
- that’s all very interesting, but how do I code for it?

## Slide 11
0
1
2
3
0
1
2
3
N
Platform: Cluster
N
N
N

## Slide 12
0
1
2
0
1
3
3
D
D
D
D
2
D
Platform: Single-System Image

## Slide 13
t0
v0
v1
v2
v3
2
0
1
3
t0
t1
t2
t3
0
1
2
3
Spatial
Tiling &
Recomposition
Time
Division
Volume
Tiling &
Recomposition
Display
Tiling
Platform: Data Decompositions

## Slide 14: Platform: Data Management
Platform: Data Management
The goal is to manage your data well
  On larger systems one technique is to use data decompositions.
  But these gains can be negated by poor management of individual subsystems or components. More later...

## Slide 15: Platform: The Points
Why learn about hardware?
  To understand how your app interacts with it
  To best utilize the hardware
  Potentially can use extra hardware features
Where?
  Platform documentation
  Talk with hardware vendor
Notes: <number>
<footer>
<header>
<date/time>
The point in any of this is to learn how your app uses different hardware, and then to write code which can better take advantage of it
again, any of these architectural diffs end up meaning that you have both
- different resources at your disposal
- different data paths which make different things ‘fast’
- example, AGP vs PCI,.number of textures, and texture ‘download’ speed.
- don’t write code for a PCI or AGP specifically, but understanding the tradeoffs means different possibilities for your app.

## Slide 16: Isn’t this a graphics course?

## Slide 17: CPU: Overview
CPU Operation
  Data transferred from main memory to registers
  CPU works on data in registers
Latency
  Registers: 0 (free)
  Level-1 (L1) cache: 1
  Level-2 (L2) cache: 10x L1
  Main memory: 100x L1
Notes: <number>
<footer>
<header>
<date/time>
- cpu to do work, op on regs
- data to regs, copied successively from memory
- describe latencies:
- closer to cpu, faster access.
- so, this makes sense, who thought of this, and why have caches,
and not just faster memory?

## Slide 18: CPU: Overview
CPU
R
L1
L2
Main
Memory
Notes: <number>
<footer>
<header>
<date/time>
- cpu to do work, op on regs
- data to regs, copied successively from memory
- describe latencies:
- closer to cpu, faster access.
- so, this makes sense, who thought of this, and why have caches,
and not just faster memory?

## Slide 19: CPU, Cache, and Memory
Caches designed to exploit data locality
  Temporal locality
  Spatial locality
Notes: <number>
<footer>
<header>
<date/time>
- caches are a tradeoff between fast and expensive, and memory
which is slow and cheap.
- different operating freqs
- caches take advantage of two observation of data properties.
- temporal locality: data which has just been used is very likely
to be used again shortly.
- example, finding the max of a set. The ‘tempmax’ variable
is often reset frequently, as new maximums are found.
- spatial locality: data which has just been accessed is likely to
be adjacent to data which will next be used. For example,
think of vertex arrays, or even individual vertices. Often placed in an array
- so, seems obvious that if my data works like that (and I make it work _more_ like that, that I’ll achieve some efficiencies. How does the cache get filled.

## Slide 20: CPU, Cache, and Memory
Main
Memory
CPU
L1
L2
Registers
Notes: <number>
<footer>
<header>
<date/time>
- caches are a tradeoff between fast and expensive, and memory
which is slow and cheap.
- different operating freqs
- caches take advantage of two observation of data properties.
- temporal locality: data which has just been used is very likely
to be used again shortly.
- example, finding the max of a set. The ‘tempmax’ variable
is often reset frequently, as new maximums are found.
- spatial locality: data which has just been accessed is likely to
be adjacent to data which will next be used. For example,
think of vertex arrays, or even individual vertices. Often placed in an array
- so, seems obvious that if my data works like that (and I make it work _more_ like that, that I’ll achieve some efficiencies. How does the cache get filled.

## Slide 21: Memory: Cache & Logical Flow
In L1?
In L2?
In Register?
Compute
Copy to L1
(10)
Copy to
Register
(1)
Copy to L2
(100)
Notes: <number>
<footer>
<header>
<date/time>
Like this
- talk a piece of data down to the cpu
Ok, so that’s logically what happens, what’ -physically- goes on?

## Slide 22: Memory: Cache & Physical Flow
CPU
Registers
Page
Main Memory
L2 Cache
L1 Cache
Notes: <number>
<footer>
<header>
<date/time>
- this is a high-level overview
-numerous details (associative vs direct cache mappings, etc)
not included - read a textbook
- read the notes for more detail

## Slide 23: Memory: Allocation & Pools
  List elements are often allocated as-needed
    This leads to spatial disparity
    Vertices, normals, textures, etc.
Notes: <number>
<footer>
<header>
<date/time>
- important to have good cache behavior for common elements
- lists are often allocated only as-needed.
- example, build a list of parts in a cad app.
- then user creates some other stuff (requiring more malloc)
- then user adds another part. That part will likely not be
contiguous with the previous parts.
- and a situation on the right top could occur
-he’s warming up to graphics

## Slide 24: Memory: Allocation & Pools
  Mitigated by use of application memory management
    Bad: malloc, malloc, malloc, malloc, ...
    Good: pools - pool_init, pool_alloc, ...
Notes: <number>
<footer>
<header>
<date/time>
- important to have good cache behavior for common elements
- lists are often allocated only as-needed.
- example, build a list of parts in a cad app.
- then user creates some other stuff (requiring more malloc)
- then user adds another part. That part will likely not be
contiguous with the previous parts.
- and a situation on the right top could occur
-he’s warming up to graphics

## Slide 25: Memory: Vertex Arrays
CAL
Notes: <number>
<footer>
<header>
<date/time>
Aha! I knew there was graphics
In this example,
- two computers
- allocate either seperate vertex /normal arrays or interleaved

## Slide 26: Graphics: Pipe
FIFO
xf
clip
light
rast
fx
fops
xf: world to screen
light: apply light
clip: clip to view
rast: convert to pixels
fx: apply texture, etc.
fops: test pixel ops
Notes: <number>
<footer>
<header>
<date/time>
-simplification of physical hardware with opengl pipe
- data buffer to lessen the effects of how fast card and data feed are
-xf: transformed from world to eye space
-light: physical lighting
- xf from eye-to-clip, and
clip

## Slide 27: Graphics: Akeley Taxonomy
  G - Generate geometric data
  T - Traverse data structures
  X - Transform primitives world to screen
  R - Rasterize triangles to pixels
  D - Display framebuffer on output device
X
R
D
G
T
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28: Graphics: Hardware
4 types of hardware are common
  G-TXRD : all hardware
  GT-XRD :
  GTX-RD :
  GTXR-D : all software
Notes: <number>
<footer>
<header>
<date/time>
1) all hardware (including the T- often a display-list cache in opengl parlance)
2) xf & rast hw
3) raster ops on hw
4) etc.
- note not all work from a phase done in hardware, but there exist some functionality in hw.
- example, do texture, but not fog.

## Slide 29: Graphics: Performance
Benchmarks
  “Trust, but verify.” - an ex-president
Definitions
  Triangle rate: speed at which primitives are transformed (X)
  Fill rate: speed at which primitives are rasterized (R)
    Depth complexity: number of times pixel filled
Caveats
  Quantization, fastpath
Notes: <number>
<footer>
<header>
<date/time>

## Slide 30: Graphics: Framerate Quantization
  Framerate quantization is the result of a buffer-swap occurring at the next vertical retrace.
    Necessary to avoid image artifacts such as tearing
  Example: 100Hz display refresh
Notes: <number>
<footer>
<header>
<date/time>

## Slide 31: Graphics: Framerate Quantization
100 Hz
50 Hz
50 Hz
33 Hz
t0
t1
t2
t3
t4
t5
t4
t6
t7
no-sync 120 Hz
: one graphics frame
tn: 1/100 second
Notes: <number>
<footer>
<header>
<date/time>

## Slide 32: Graphics: Fastpath
Definition
  Fastpath: the most optimized path through graphics hardware (and driver software)
Example
  fast path: float verts, float norms, AGBR textures, z-test
  less fast path: float verts, float norms, RGBA textures, z-test
Notes: <number>
<footer>
<header>
<date/time>

## Slide 33: Graphics: Fastpath Example
Notes: <number>
<footer>
<header>
<date/time>

## Slide 34: Graphics: Fastpath Points
  Fast path is often synonymous with ideal path.
    Real usage of graphics falls on a continuum.
Fast path
(hardware)
Slow path
(software)
Speed
Quality
Where is your application?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 35: Graphics: Fastpath Points
  Must quantify what hardware can do
    know the platform
    test at runtime
  What can your application do
    what quality do you need, and when
    what speed do you need, and when
Notes: <number>
<footer>
<header>
<date/time>

## Slide 36: Graphics Hardware: Testing
Duplicate performance numbers simply:
  Good: build a simple test program
  Better: SPECglperf™ - http://www.spec.org
Maximize performance in an app:
  Good: Use fast API extensions
  Better: Create an “is-fast” test, use what is verified as fast

## Slide 37: Graphics Hardware: “Is-Fast”
Test each platform to determine fast path
  Once, per-machine, test primitives and modes
    Vertex array format, texture format, display list, etc.
  Store data in database
    Detect hardware changes or time-to-live
  Read data from database at startup
    Check database or re-generate data
Notes: <number>
<footer>
<header>
<date/time>
once, per-machine, at app startup, generate data. vertex arrays, display lists, texture formats, etc.
  store data in database, per-machine, also keep a time-to-live for this data.
  at app startup, check database, or re-generate data.

## Slide 38: Think Globally, Act Locally
Think globally
  Know the platforms & graphics hardware
  Use hardware effectively in your app
  Balance hardware utilization
Notes: <number>
<footer>
<header>
<date/time>